## Slide 1: ಲೋಡ್ ಮಾಡಿದ ಸ್ಪ್ರಿಂಗ್
Engineering Academy | ಘಟಕ 3

## Slide 2: ಚಟುವಟಿಕೆ 1: ಒಂದು ಇಲಿಕತ್ತರಿ ಅಥವಾ ಮೌಸ್‌ಟ್ರ್ಯಾಪ್‌ ಬ್ಯಾಟರಿ ಆಗಬಲ್ಲದೇ?
ಚಟುವಟಿಕೆ 1
Notes: https://commons.wikimedia.org/wiki/File:Victor-Mousetrap.jpg

## Slide 3
ಬ್ಯಾಟರಿ ಎಂದರೇನು?
Notes: Start by asking the group to describe and explain what a battery is.
https://www.engineersgarage.com/introduction-batteries-their-types/

## Slide 4
ಸಂಗ್ರಹವಾಗಿರುವ ರಾಸಾಯನಿಕ ಶಕ್ತಿಯನ್ನು ರಾಸಾಯನಿಕ ಕ್ರಿಯೆಯ ಮೂಲಕ ನೇರವಾಗಿ ವಿದ್ಯುತ್ ಶಕ್ತಿಯನ್ನಾಗಿ ಪರಿವರ್ತಿಸುವ ಒಂದು ಸಾಧನ.
Notes: One of the most common definitions is that a battery is a device that converts stored chemical energy directly into electric energy by means of a chemical reaction. Show the group the variety of batteries you have on hand.
https://www.officenational.com.au/shop/en/sba/duracell-alkaline-battery-coppertop-d

## Slide 5
ವಿಶ್ವದ ಅತಿದೊಡ್ಡ ಬ್ಯಾಟರಿ ಯಾವುದು?
Notes: Now ask the group what they think the world’s biggest battery is. Where is it? What does it look like? How much power can it store?

## Slide 6
Notes: Play the video called The world's biggest battery looks nothing like a battery (5:15) which describes pumped hydro schemes as the world’s biggest batteries.

## Slide 7
ಮೌಸ್‌ಟ್ರ್ಯಾಪ್‌ ಹೇಗೆ ಕೆಲಸ ಮಾಡುತ್ತದೆ?
Notes: Now show the group a mousetrap and demonstrate how it works.
https://commons.wikimedia.org/wiki/File:Victor-Mousetrap.jpg

## Slide 8
Notes: Ask them whether they think this mousetrap can be thought of as a battery. Why or why not? You can facilitate this discussion using the following questions.
  What do batteries basically do? (They store energy.)
  What do you have to do to set the mousetrap? (You have use energy to push against the spring at set the trap.)
  What happens if you trigger the mousetrap? (The energy stored in the spring is released and the trap snaps shut.)
Explain that a mousetrap can be thought of as a battery. Batteries are basically just energy storage devices. We put energy into the battery, and it stays there until we release it. We must put energy in to bend the spring and set the mousetrap. This energy stays inside the spring until the mousetrap is triggered. Then all this energy is released very quickly as the trap snaps shut.

## Slide 9
ಈ ಕುರಿತು ಆಲೋಚಿಸಿ
  ನಾವು ಮೌಸ್‌ಟ್ರ್ಯಾಪ್‌ ಅನ್ನು ಬ್ಯಾಟರಿಯಾಗಿ ಬಳಸಬಹುದಾದರೆ, ಇನ್ನು ಯಾವುದನ್ನು ಬ್ಯಾಟರಿಯಾಗಿ ಬಳಸಬಹುದು? ಶಕ್ತಿಯು ಎಲ್ಲಿ ಅಥವಾ ಹೇಗೆ ಸಂಗ್ರಹವಾಗುತ್ತದೆ?
  ಮೌಸ್‌ಟ್ರ್ಯಾಪ್‌ ಬ್ಯಾಟರಿಯಿಂದ ಓಡುವ ಕಾರನ್ನು ನಾವು ವಿನ್ಯಾಸಗೊಳಿಸಬಹುದೇ? ಇದನ್ನು ಸಾಧ್ಯವಾಗಿಸಲು ನಾವು ಯಾವ ರೀತಿಯ ಸಮಸ್ಯೆಗಳನ್ನು ಪರಿಹರಿಸಬೇಕಾಗುತ್ತದೆ?
  ಮೌಸ್‌ಟ್ರ್ಯಾಪ್‌ ಬ್ಯಾಟರಿಯಿಂದ ನಾವು ಬೇರೆ ಇನ್ಯಾವ ವಸ್ತುಗಳಿಗೆ ಶಕ್ತಿ ನೀಡಬಹುದು?
Notes: Split the group into their teams for this challenge and ask them to think about the following questions. They can note their answers in Section 1 of their workbooks.
If we can use a mousetrap as a battery, what else could we use as a battery? Where or how would the energy be stored?
Could we design a car that runs on a mousetrap battery? What kinds of problems would we need to solve to make this possible?
What else might we power with a mousetrap battery?
After about 10 min bring students back together and have them share and discuss their answers.

## Slide 10: ನಿಮ್ಮ ವಿನ್ಯಾಸದ ಸವಾಲು
  ವಾಹನವು ಕನಿಷ್ಠ ಮೂರು ಚಕ್ರಗಳನ್ನು ಹೊಂದಿರಬೇಕು.
  ವಾಹನವನ್ನು ಒಂದು ಬಾರಿ 'ಚಾರ್ಜ್' ಮಾಡಿದಾಗ ಅದು ಕನಿಷ್ಠ 10 ಮೀಟರ್ (32.8 ಅಡಿ) ದೂರವನ್ನು ಕ್ರಮಿಸುವ ಸಾಮರ್ಥ್ಯ ಹೊಂದಿರಬೇಕು.
  ವಾಹನವನ್ನು ತಳ್ಳಿ ಚಾಲನೆ ಮಾಡುವುದಕ್ಕೆ ಅನುಮತಿ ಇರುವುದಿಲ್ಲ.
  ವಿದ್ಯಾರ್ಥಿಗಳು ನಿಗದಿತ ಸಮಯದಲ್ಲಿ ತಮ್ಮ ವಾಹನಗಳನ್ನು ವಿನ್ಯಾಸಗೊಳಿಸಬೇಕು ಮತ್ತು ನಿರ್ಮಿಸಬೇಕು.
ಮಾನದಂಡ
ಮಿತಿಗಳು
Notes: Tell students that they are going to design and build a vehicle powered by a mousetrap. Describe the criteria and the constraints for the challenge and have teams write these down in Section 2 of their workbooks.
  Success criteria
    The vehicle must have at least three wheels.
    The vehicle must be able to cover a minimum distance of 10 m on a single ‘charge’.
  Constraints
    No push starts of vehicles are allowed.
    Students must design and build their vehicles within the given time.

## Slide 11: ಇಂಜಿನಿಯರಿಂಗ್ ವಿನ್ಯಾಸ ಪ್ರಕ್ರಿಯೆ
ಸಮಸ್ಯೆಯನ್ನು ಗುರುತಿಸಿ ಮತ್ತು ವಿವರಿಸಿ
1
ಮಾಹಿತಿಯನ್ನು ಸಂಗ್ರಹಿಸಿ
2
ಸಂಭವನೀಯ ಪರಿಹಾರಗಳನ್ನು ರಚಿಸಿ
3
ಮೂಲಮಾದರಿಯನ್ನು ರಚಿಸಿ
4
ಮೂಲಮಾದರಿಯನ್ನು ಪರೀಕ್ಷಿಸಿ ಮತ್ತು ಮೌಲ್ಯಮಾಪನ ಮಾಡಿ
5
ಪರಿಹಾರ ಮಾರ್ಗವನ್ನು ಪರಿಷ್ಕರಿಸಿ ಮತ್ತು/ಅಥವಾ ಮರುವಿನ್ಯಾಸಗೊಳಿಸಿ
6
ಪರಿಹಾರ ಮಾರ್ಗವನ್ನು ಪ್ರಸ್ತುತಪಡಿಸಿ ಅಥವಾ ತಿಳಿಸಿ
7
ಸಮಸ್ಯೆಯನ್ನು ಗುರುತಿಸಿ ಮತ್ತು ವಿವರಿಸಿ
1
Notes: Tell students that they will follow the engineering design process. If your students have never used the engineering design process before, hand out a copy of The Engineering Design Process to each team and take some time to explain the process and its steps.

## Slide 12: ರೇಸ್‌ನ ಸಮಯ!
ಸಹಿಷ್ಣುತೆಯ ಓಟ
ಒಂದು ಬಾರಿ 'ಚಾರ್ಜ್' ಮಾಡಿದಾಗ ಅತಿ ಹೆಚ್ಚು ದೂರ ಕ್ರಮಿಸುವ ಅಥವಾ ನಿರ್ದಿಷ್ಟ ಸಮಯದಲ್ಲಿ ಅತಿ ಹೆಚ್ಚು ಬಾರಿ ಚಾರ್ಜ್ ಮಾಡಿ ಹೆಚ್ಚು ದೂರ ಕ್ರಮಿಸುವ ವಾಹನ.
ವೇಗದ ಓಟ
ನಿರ್ದಿಷ್ಟ ದೂರವನ್ನು ಅತ್ಯಂತ ವೇಗವಾಗಿ ಕ್ರಮಿಸುವ ವಾಹನ.
Notes: Explain that teams will compete in races against other teams:
  An endurance race where prizes will be awarded for the vehicle that covers the greatest distance on a single ‘charge’.
  A speed race where prizes will be awarded for the fastest vehicle over a specific distance.

## Slide 13
ನಿಮ್ಮ ವಿನ್ಯಾಸದ ಪರಿಹಾರವನ್ನು ಪ್ರಸ್ತುತಪಡಿಸಿ ಮತ್ತು ನಿಮ್ಮ ವಿನ್ಯಾಸದ ಕಥೆಯನ್ನು ವಿವರಿಸಿ
ಘರ್ಷಣೆಗೆ ಸಂಬಂಧಿಸಿದಂತೆ ನೀವು ಎದುರಿಸಿದ ಸಮಸ್ಯೆಗಳು ಯಾವುವು ಮತ್ತು ನಿಮ್ಮ ತಂಡವು ಅವುಗಳನ್ನು ಹೇಗೆ ಪರಿಹರಿಸಿತು?
ನೀವು ಯಾವ ರೀತಿಯ ಚಕ್ರಗಳನ್ನು ಬಳಸಿದ್ದೀರಿ? ನೀವು ಅವುಗಳನ್ನೇ ಏಕೆ ಆರಿಸಿಕೊಂಡಿದ್ದೀರಿ?
ನಿಮ್ಮ ಮೌಸ್‌ಟ್ರ್ಯಾಪ್‌ ಸಂಗ್ರಹವಾದ ಒಟ್ಟು ಅಂದಾಜು ಸ್ಥಿತಿಸ್ಥಾಪಕ (ಇಲಾಸ್ಟಿಕ್) ಅಂತಸ್ಥ ಶಕ್ತಿ (ಪೊಟೆನ್ಶಿಯಲ್ ಎನರ್ಜಿ) ಎಷ್ಟು?
ವಾಹನದ ಒಟ್ಟು ಯಾಂತ್ರಿಕ ಪ್ರಯೋಜನ ಎಷ್ಟು?
ಘರ್ಷಣೆಯನ್ನು ಮೀರಲು ನಿಮ್ಮ ವಾಹನವು ಮಾಡಿದ ಕೆಲಸದ ಪ್ರಮಾಣವೆಷ್ಟು?
ವಾಹನವು ಚಾಲನೆಯಲ್ಲಿರುವಾಗ ಅದರ ವೇಗೋತ್ಕರ್ಷ ಎಷ್ಟಿತ್ತು?
ನಿಮ್ಮ ಮೌಸ್‌ಟ್ರಾಪ್ ವಾಹನವು ತಲುಪಿದ ಗರಿಷ್ಠ ವೇಗ ಎಷ್ಟು?
ವಾಹನವು ಕ್ರಮಿಸಬಹುದಾದ ಸೈದ್ಧಾಂತಿಕ ದೂರಕ್ಕೂ ಮತ್ತು ಅದು ವಾಸ್ತವವಾಗಿ ಕ್ರಮಿಸಿದ ದೂರಕ್ಕೂ ಇರುವ ಹೋಲಿಕೆ ಏನು ಮತ್ತು ಈ ವ್ಯತ್ಯಾಸಕ್ಕೆ ಕಾರಣವೇನು?
ನಿಮ್ಮ ವಾಹನದ ಚಲನೆಗೆ ವಿರುದ್ಧ ದಿಕ್ಕಿನಲ್ಲಿ ಕಾರ್ಯನಿರ್ವಹಿಸುತ್ತಿದ್ದ ಘರ್ಷಣಾ ಬಲ ಎಷ್ಟಿತ್ತು?
ಅಂತಸ್ಥ ಶಕ್ತಿಯನ್ನು ಚಲನಶಕ್ತಿಯನ್ನಾಗಿ ಪರಿವರ್ತಿಸುವಲ್ಲಿ ವಾಹನದ ಒಟ್ಟು ದಕ್ಷತೆ ಎಷ್ಟಿತ್ತು? ಹೆಚ್ಚಿನ ಆಪ್ಟಿಮೈಸೇಶನ್ ಮೂಲಕ ಇದನ್ನು ಹೇಗೆ ಸುಧಾರಿಸಬಹುದು?
ಸಾರ್ವಜನಿಕ ಪ್ರಸ್ತುತಿ
Notes: Explain that teams will also present their vehicles to a public audience. This will also include them telling the story of their design, testing, and redesign process and presenting answers to the following questions:
  What problems related to friction did they encounter and how did they overcome these?
  What kind of wheels did they use? Why did they choose them?
  What was the total approximate elastic potential energy stored in their mousetrap?
  What was the total mechanical advantage of their vehicle?
  What was the work done by their vehicle in overcoming friction?
  What was the acceleration of their vehicle while under power?
  What was the maximum velocity achieved by their mousetrap vehicle?
  How did the theoretical distance their vehicle might have covered compare to the actual distance it covered and what was responsible for this difference?
  What was the force of friction acting in the opposite direction to the motion of their vehicle?
  What was the overall efficiency of their vehicle in converting potential energy to kinetic energy? How might this be improved through additional optimization?
Teams must also be prepared to answer questions on their design and the process they followed from members of the audience.
This presentation must be no more than 10 minutes.
Encourage teams to take pictures, record videos, and keep detailed notes of what they do and how they do it throughout the challenge. All this media and information will be especially useful come time to create their presentation.

## Slide 14: ಚಟುವಟಿಕೆ 2: ಸಮಸ್ಯೆಯನ್ನು ಗುರುತಿಸಿ ಮತ್ತು ವಿವರಿಸಿ
ಸಮಸ್ಯೆಯನ್ನು ಗುರುತಿಸಿ ಮತ್ತು ವಿವರಿಸಿ
ಸಮಸ್ಯೆಯನ್ನು ಗುರುತಿಸಿ ಮತ್ತು ವಿವರಿಸಿ
1
ಮಾಹಿತಿಯನ್ನು ಸಂಗ್ರಹಿಸಿ
2
ಸಂಭವನೀಯ ಪರಿಹಾರಗಳನ್ನು ರಚಿಸಿ
3
ಮೂಲಮಾದರಿಯನ್ನು ರಚಿಸಿ
4
ಮೂಲಮಾದರಿಯನ್ನು ಪರೀಕ್ಷಿಸಿ ಮತ್ತು ಮೌಲ್ಯಮಾಪನ ಮಾಡಿ
5
ಪರಿಹಾರ ಮಾರ್ಗವನ್ನು ಪರಿಷ್ಕರಿಸಿ ಮತ್ತು/ಅಥವಾ ಮರುವಿನ್ಯಾಸಗೊಳಿಸಿ
6
ಪರಿಹಾರ ಮಾರ್ಗವನ್ನು ಪ್ರಸ್ತುತಪಡಿಸಿ ಅಥವಾ ತಿಳಿಸಿ
7
ಸಮಸ್ಯೆಯನ್ನು ಗುರುತಿಸಿ ಮತ್ತು ವಿವರಿಸಿ
1

## Slide 15
ಒಂದು ವಸ್ತುವನ್ನು ಚಲಿಸುವಂತೆ ಮಾಡಲು ಏನು ಬೇಕು?
Notes: Start by facilitating a discussion with the group about what is needed to make an object move. Demonstrate this by having a student push a chair (or another object) across the floor. Say that to move the chair, the student must do work and to do work, the student needs to expend energy.
https://www.shutterstock.com/search/chair-race

## Slide 16
ಶಕ್ತಿ ಎನ್ನುವುದು ಕೆಲಸ ಮಾಡುವ ಸಾಮರ್ಥ್ಯವಾಗಿದೆ
Notes: Therefore, energy is defined as the “ability to do work”. The more work that must be done to move something, the more energy is needed.

## Slide 17
ಚಲನಶಕ್ತಿ
Notes: Explain that there are two main forms of energy – kinetic energy and potential energy.
  Kinetic energy is the energy of a moving object like a wrecking ball swinging into a house. It has kinetic energy enough to destroy a building. Demonstrate that a ball thrown through the air also has kinetic energy. If thrown at a window, it might have enough energy to break the window. Have the group give other everyday examples of things with kinetic energy.
  Potential energy is the energy that is stored because of the position or arrangement of matter. An example is a stationary wrecking ball held above a car. It is not doing any work on the car but sure has the potential to do some work if released. This is called gravitational potential energy (the potential energy of an object because of its position in Earth’s gravitational field). Demonstrate that a ball held above the ground also has gravitational potential energy that get converted into kinetic energy when released. Other types of potential energy include:

## Slide 18
ಅಂತಸ್ಥ ಶಕ್ತಿ
Notes: Potential energy is the energy that is stored because of the position or arrangement of matter. An example is a stationary wrecking ball held above a car. It is not doing any work on the car but sure has the potential to do some work if released. This is called gravitational potential energy (the potential energy of an object because of its position in Earth’s gravitational field). Demonstrate that a ball held above the ground also has gravitational potential energy that get converted into kinetic energy when released.

## Slide 19: ಅಂತಸ್ಥ ಶಕ್ತಿಯ ಪ್ರಮುಖ ವಿಧಗಳು
ವಸ್ತುವು ನೆಲದಿಂದ ಮೇಲಿರುವ ಅದರ ಸ್ಥಾನದ ಆಧಾರದ ಮೇಲೆ ಕೆಲಸ ಮಾಡುವ ಸಾಮರ್ಥ್ಯ.
ಪರಮಾಣುಗಳು ಮತ್ತು ಅಣುಗಳ ನಡುವಿನ ರಾಸಾಯನಿಕ ಬಂಧಗಳಲ್ಲಿ ಸಂಗ್ರಹವಾಗಿರುವ ಶಕ್ತಿ.
ರಬ್ಬರ್ ಬ್ಯಾಂಡ್ ಅಥವಾ ಸ್ಪ್ರಿಂಗ್‌ನಂತಹ ವಸ್ತುವನ್ನು ಎಳೆದಾಗ ಅಥವಾ ಅದರ ಆಕಾರ ಬದಲಾದಾಗ ಸಂಗ್ರಹವಾಗುವ ಶಕ್ತಿ.
ವಿದ್ಯುತ್ ಕ್ಷೇತ್ರದಲ್ಲಿ ಚಾರ್ಜ್‌ ಹೊಂದಿರುವ ಕಣದ ಸ್ಥಾನದಿಂದಾಗಿ ಅಥವಾ ಇನ್ನೊಂದು ಚಾರ್ಜ್‌ ಹೊಂದಿರುವ ಕಣಕ್ಕೆ ಸಂಬಂಧಿಸಿದಂತೆ ಅದರ ಸ್ಥಾನದಿಂದಾಗಿ ಸಂಗ್ರಹವಾಗುವ ಶಕ್ತಿ.
ಗುರುತ್ವಾಕರ್ಷಣ ಅಂತಸ್ಥ ಶಕ್ತಿ
ರಾಸಾಯನಿಕ ಅಂತಸ್ಥ ಶಕ್ತಿ
ಸ್ಥಿತಿಸ್ಥಾಪಕ (ಇಲಾಸ್ಟಿಕ್) ಅಂತಸ್ಥ ಶಕ್ತಿ
ವಿದ್ಯುತ್‌ ಅಂತಸ್ಥ ಶಕ್ತಿ
Notes: Chemical potential energy is the energy stored in the chemical bonds between atoms and molecules. Have the group give examples of everyday substances we use because of their chemical potential energy.
Elastic potential energy is the energy stored when an object, like a rubber band or spring is stretched or deformed. This energy is released when the object regains its normal shape. Have the group give other everyday examples of things able to store elastic potential energy.
Electric (or electromagnetic) potential energy is the energy stored because of a charged particle’s position in an electric field or its position relative to another charged particle. Demonstrate this by holding two opposite magnetic poles apart. As soon as we let go, this potential energy is converted into the kinetic energy of the magnets as they move together.

## Slide 20
ವಿಭಾಗ 3 ಅನ್ನು ಓದಿ ಮತ್ತು ಲೆಕ್ಕಾಚಾರಗಳನ್ನು ಮಾಡಿ
Notes: Have teams read through Section 3 in their workbooks and do the simple calculations on kinetic energy.

## Slide 21: 3.2 m/s ವೇಗದಲ್ಲಿ ಚಲಿಸುತ್ತಿರುವ 0.45 kg ತೂಕದ ಮೌಸ್‌ಟ್ರ್ಯಾಪ್ ವಾಹನದ ಚಲನಶಕ್ತಿ ಎಷ್ಟಿರುತ್ತದೆ?
Notes: Spend a few minutes reviewing the answers to the questions from Section 3 in the student workbook with the group to make sure everyone understands how to work with the kinetic energy formula.

## Slide 22: ಒಂದು ಮೌಸ್‌ಟ್ರ್ಯಾಪ್ ವಾಹನವು 1.46 J ಚಲನ ಶಕ್ತಿಯನ್ನು ಹೊಂದಿರುತ್ತದೆ. ಅದರ ದ್ರವ್ಯರಾಶಿ 327 g ಆಗಿದ್ದರೆ, ಅದರ ವೇಗವು ಎಷ್ಟು?

## Slide 23
ರಾಸಾಯನಿಕ ಅಂತಸ್ಥಶಕ್ತಿ
ಉಷ್ಣ ಶಕ್ತಿ
ಚಲನ ಶಕ್ತಿ
Notes: Explain that cars that use gasoline or petrol convert the chemical potential energy in the fuel into thermal energy in the cylinders which then gets converted into the kinetic energy of the pistons which ultimately turns the wheels and drives the car forward.
https://www.wonderopolis.org/wonder/what-is-gasoline-made-of
https://www.istockphoto.com/search/2/image?phrase=car+explosion
https://www.kbb.com/car-advice/horsepower-vs-torque/

## Slide 24
ವಿಭಾಗ 4 ಅನ್ನು ಓದಿ ಮತ್ತು ಪ್ರಶ್ನೆಗಳಿಗೆ ಉತ್ತರಿಸಿ
Notes: In this challenge we need to find a way to convert the elastic potential energy of a mousetrap into the kinetic energy of the vehicle.
Have teams read through Section 4 of their workbooks and then answer the questions.

## Slide 25
ಯಾವುದೇ ಬಾಹ್ಯ ಬಲವು ಕಾರ್ಯನಿರ್ವಹಿಸದ ಹೊರತು, ಸ್ಥಿರವಾಗಿರುವ ವಸ್ತುವು ಸ್ಥಿರವಾಗಿಯೇ ಇರುತ್ತದೆ.
ಘರ್ಷಣೆಯು (ಮೇಲ್ಮೈ ಮತ್ತು ದ್ರವ) ಎಲ್ಲಾ ಚಲಿಸುವ ವಸ್ತುಗಳನ್ನು ನಿಲ್ಲಿಸಲು ಪ್ರಯತ್ನಿಸುತ್ತದೆ.
ಒಟ್ಟು ಬಲವು ಹೆಚ್ಚಾದಷ್ಟೂ, ವೇಗೋತ್ಕರ್ಷ ಅಥವಾ ಚಲನೆಯಲ್ಲಿನ ಬದಲಾವಣೆ ಹೆಚ್ಚಾಗಿರುತ್ತದೆ.
ಘರ್ಷಣಾ ಬಲಕ್ಕೆ ಸಮನಾದ ಅಥವಾ ಅದಕ್ಕಿಂತ ಹೆಚ್ಚಿನ ಬಲವನ್ನು ಪ್ರಯೋಗಿಸದ ಹೊರತು, ಚಲಿಸುತ್ತಿರುವ ವಸ್ತುವು ವೇಗವನ್ನು ಕಳೆದುಕೊಳ್ಳುತ್ತದೆ.
ಒಂದೇ ಪ್ರಮಾಣದ ಬಲದ ಅಡಿಯಲ್ಲಿ, ಹಗುರವಾದ ವಸ್ತುಗಳು ವೇಗವಾಗಿ ವೇಗೋತ್ಕರ್ಷಗೊಳ್ಳುತ್ತವೆ.
ಘರ್ಷಣೆ ಕಡಿಮೆಯಾದಷ್ಟೂ, ವ್ಯರ್ಥವಾಗುವ ಚಲನಶಕ್ತಿಯು ಕಡಿಮೆಯಾಗುತ್ತದೆ.
ಕಡಿಮೆ ಘರ್ಷಣೆ ಇದ್ದಷ್ಟೂ, ಚಲನ ಶಕ್ತಿ ಕಳೆದುಕೊಳ್ಳುವಿಕೆ ಕಡಿಮೆಯಾಗುತ್ತದೆ.
ಪ್ರಮುಖ ಅಂಶಗಳು
Notes: Go through the basic answers to the questions in Section 4 of the student workbook to make sure that everyone understands the basics of the laws of motion and friction. Here are some suggested answers for each question.
  An object, such as a car, at rest will remain at rest unless an external force acts on it.
  The reason moving cars don’t keep moving is because friction (surface and fluid) is constantly converting kinetic energy of the vehicle into heat and sound.
  If the engine of a car provides a force greater than friction (and air resistance), the car will accelerate and gain speed. The greater the net force, the greater the acceleration.
  Unless the engine continues to provide a force greater than friction (and air resistance), a car will slow down and eventually stop.
  Cars that are lighter will experience greater acceleration than heavier cars when the same net force is applied to them, or will need a smaller net force to achieve the same acceleration.
  The smaller the force of friction a car experiences, the smaller the force needed to accelerate the car (or change its motion).
  The smaller the force of friction a car experiences, the less kinetic energy will be lost to heat and sound and the farther the car will travel with a given force.

## Slide 26: ಚಟುವಟಿಕೆ 3: ಮಾಹಿತಿಯನ್ನು ಸಂಗ್ರಹಿಸಿ
ಸಮಸ್ಯೆಯನ್ನು ಗುರುತಿಸಿ ಮತ್ತು ವಿವರಿಸಿ
ಸಮಸ್ಯೆಯನ್ನು ಗುರುತಿಸಿ ಮತ್ತು ವಿವರಿಸಿ
1
ಮಾಹಿತಿಯನ್ನು ಸಂಗ್ರಹಿಸಿ
2
ಸಂಭವನೀಯ ಪರಿಹಾರಗಳನ್ನು ರಚಿಸಿ
3
ಮೂಲಮಾದರಿಯನ್ನು ರಚಿಸಿ
4
ಮೂಲಮಾದರಿಯನ್ನು ಪರೀಕ್ಷಿಸಿ ಮತ್ತು ಮೌಲ್ಯಮಾಪನ ಮಾಡಿ
5
ಪರಿಹಾರ ಮಾರ್ಗವನ್ನು ಪರಿಷ್ಕರಿಸಿ ಮತ್ತು/ಅಥವಾ ಮರುವಿನ್ಯಾಸಗೊಳಿಸಿ
6
ಪರಿಹಾರ ಮಾರ್ಗವನ್ನು ಪ್ರಸ್ತುತಪಡಿಸಿ ಅಥವಾ ತಿಳಿಸಿ
7
ಮಾಹಿತಿಯನ್ನು ಸಂಗ್ರಹಿಸಿ
2

## Slide 27
ಮೌಸ್‌ಟ್ರ್ಯಾಪ್‌ ಸುರಕ್ಷತೆಯ ಸಲಹೆಗಳು
  ಟ್ರ್ಯಾಪ್ ಅನ್ನು ಎಂದಿಗೂ ಸಿದ್ಧಗೊಳಿಸಿದ ನಂತರ ಹಾಗೆಯೇ ಬಿಡಬೇಡಿ.
  ಟ್ರ್ಯಾಪ್ ಅನ್ನು ಕೈಯಲ್ಲಿ ಹಿಡಿದಿರುವಾಗ ಎಂದಿಗೂ ಸಕ್ರಿಯಗೊಳಿಸಬೇಡಿ. ಯಾವಾಗಲೂ ಅದನ್ನು ಒಂದು ಮೇಲ್ಮೈ ಮೇಲೆ ಇಟ್ಟು ಬಳಸಿ.
  ಟ್ರ್ಯಾಪ್ ಅನ್ನು ಎಂದಿಗೂ ನಿಮ್ಮ ಬೆರಳಿನಿಂದ ಟ್ರಿಗರ್ ಮಾಡಬೇಡಿ. ಯಾವಾಗಲೂ ಪೆನ್, ಪೆನ್ಸಿಲ್ ಅಥವಾ ಇತರ ವಸ್ತುವನ್ನು ಬಳಸಿ.
Notes: Have students get into their teams and give each team its mousetrap for this challenge. Show students how to set and trigger the trap being very clear about the following safety rules:
  Never leave the trap set
  Never trigger the trap while holding it. Always lay it on a surface.
  Never trigger the trap with your finger. Always use a pen, pencil or other object.
Allow teams to practice setting and triggering the trap a few times making sure that everyone adheres to the three safety rules.
Ask teams to describe how the trap closes when triggered. Does it move quickly or slowly? Is the elastic potential energy in the spring released quickly of slowly? How far does the trap arm move when closing?
Have teams set and trigger their traps and ask them what would happen if they somehow connected the trap arms directly to the wheels of their vehicles. What do they think would happen? How far would their vehicles travel. How effective would this approach be?
Ask the group if anyone has any suggestions about how the elastic potential energy stored in the mousetrap can be released in a more controlled manner over a longer period.
https://www.canr.msu.edu/news/safety_awareness_to_prevent_later_injuries_to_others

## Slide 28
Notes: Play the video called The mighty mathematics of the lever (4:45) to the group that introduces and explains the concepts of levers.

## Slide 29
Notes: Emphasize that levers do not violate the laws of physics. We know that . If we extend the distance over which the force is applied to reduce the force, the total work is still the same. We have made a trade-off - reduced force but applied over a greater distance. Nothing is free!
Emphasize that levers do not violate the laws of physics. We know that 𝑊=𝐹×𝑑. If we extend the distance over which the force is applied to reduce the force, the total work is still the same. We have made a trade-off - reduced force but applied over a greater distance. Nothing is free!

## Slide 30
10 kg
5 kg
7 m
14 m
Notes: Work through the numerical example of this

## Slide 31
Notes: Explain that mechanical advantage is a measure of this trade-off and is the ratio of the output force to the input force. For a lever, it can also be expressed as the ratio of the distance of the input force from the fulcrum to the distance of the output force from the fulcrum.

## Slide 32
ಯಾಂತ್ರಿಕ ಪ್ರಯೋಜನ ಎಂದರೆ ಒಂದು ಸರಳ ಯಂತ್ರವು ಬಲವನ್ನು ಅಥವಾ ದೂರವನ್ನು ವರ್ಧಿಸುವ ಪರಿಣಾಮವಾಗಿದೆ. ಅಂತಹ ಸರಳ ಯಂತ್ರಗಳಿಗೆ ಉದಾಹರಣೆಗಳು:
ಸನ್ನೆಕೋಲು
ಇಳಿಜಾರು ಸಮತಲ
ಚಕ್ರ ಮತ್ತು ಅಚ್ಚು
ರಾಟೆಯ ವ್ಯವಸ್ಥೆ
ಬೆಣೆ
ತಿರುಪು ಮೊಳೆ
Notes: Simple machines - https://www.generationgenius.com/simple-machines-reading-material/ (fair use)

## Slide 33
ಔಟ್‌ಪುಟ್:
ಹೆಚ್ಚಿನ ದೂರದ ಮೇಲೆ ಪ್ರಯೋಗವಾಗುವ ಕಡಿಮೆ ಬಲ.
ಇನ್‌ಪುಟ್:
ಕಡಿಮೆ ದೂರದ ಮೇಲೆ ಪ್ರಯೋಗಿಸುವ ಹೆಚ್ಚಿನ ಬಲ.
Notes: Explain that the distance can also be measured as the distance over which the input and output forces travel.

## Slide 34
MA > 1
ಔಟ್‌ಪುಟ್ ಬಲ > ಇನ್‌ಪುಟ್ ಬಲ
ಔಟ್‌ಪುಟ್ ದೂರ < ಇನ್‌ಪುಟ್ ದೂರ
MA < 1
ಔಟ್‌ಪುಟ್ ಬಲ < ಇನ್‌ಪುಟ್ ಬಲ
ಔಟ್‌ಪುಸ್ ದೂರ > ಇನ್‌ಪುಟ್ ದೂರ
Notes: Explain that
  A mechanical advantage greater than one means that
    The output force is greater than the input force
    The output force travels a smaller distance than the input force
  A mechanical advantage less than one means that the output force
    The output force is less than the input force
    The output force travels a greater distance than the input force

## Slide 35
ಹಾಕುವ ಬಲ
ಹೆಚ್ಚಿನ ದೂರ
ಕಡಿಮೆ ದೂರ
ಫಲ್ಕ್ರಮ್ (ಆಧಾರ ಬಿಂದು)
ಹೊರೆ
Notes: Explain that we can arrange a lever with both arms on the same side of the pivot. The force at the end of the shorter arm would be greater than the force at the end of the longer arm but it would travel through a smaller distance.
https://letstalkscience.ca/educational-resources/backgrounders/simple-machines-levers

## Slide 36
Notes: Explain that we can arrange a lever with both arms on the same side of the pivot. The force at the end of the shorter arm would be greater than the force at the end of the longer arm but it would travel through a smaller distance.

## Slide 38
ವಿಭಾಗ 5 ರ ಮೂಲಕ ಕೆಲಸ ಮಾಡಿ
Notes: Give each team a wooden dowel or skewer, some cable ties or electrical tape and a ruler and ask them to work through the steps in Section 5 of their workbooks to explore how they can change the mechanical advantage of their mousetraps.

## Slide 39
45 mm
295 mm
Notes: Go through the answers to the questions in Section 5 of the student workbook, especially question 8. Do the calculation of the mechanical advantage based on the actual length of the mousetrap arm and dowels or skewers teams were working with.
  Measure the length of your mousetrap spring arm in mm.
  Calculate the length of the arc through which the mousetrap arm travels as it closes. Remember that the circumference of a circle is where is the radius of the circle.
  Note: some mousetraps do not operate over a full 180o. You may need to approximate the percentage of the semi-circle through which the arm does travel and multiply your answer by this amount. For example, if the arm travels through 90% of the semi-circle, multiply the answer by 0.9.
3. If you connected the wheels of a vehicle directly to the mousetrap arm, what do you think would happen? How far would the vehicle travel?
The trap would snap shut very quickly, transferring its energy to the wheels very quickly. The wheels would accelerate rapidly but only for a very short period of time. It is likely that the wheels would just spin without driving the car forward very much, if at all.
4. Using the materials you have, create a device that will reduce the size of the output force and make it be applied over a greater distance.
Teams should figure out that if they extend the length of the mousetrap arm, they will increase the distance (and hence) time over which the force is applied and also decrease the force applied to the wheels.
5. If you have not yet done so, connect your dowel or skewer to the mousetrap arm with the cable ties or electrical tape. Which arm, the original arm or the extended arm travels through a greater distance?
The extended arm travels through a greater distance. Encourage students to trace, on a piece of paper, the arcs made by the end of the original arm and the extended arm to see that this is the case.
6. Is the force greater at the end of the original arm or the extended arm? Why?
The force is greater at the end of the original arm. The force at the end of the extended arm is being applied over a greater distance. For the work being done at both point to still be the same, the force must be reduced? Students should be able to feel this is the case by moving the trap from the end of the original arm and the end of the extended arm.
7. Measure the length of the extended arm and calculate the arc length through which the end travels.
8. We can think of the original arm as the input arm and the extended arm as the output arm. Calculate the mechanical advantage of this simple machine.
  9. By creating this simple lever machine with a mechanical advantage less than one, we increase the distance through which the output force is applied while decreasing the magnitude of this output force. How will this help us design a better mousetrap vehicle?
  It will reduce the force applied by the mousetrap to the wheels, preventing them from slipping and the vehicle wheel spinning. This reduced force is also applied over a greater distance meaning that we can drive the wheels for longer. While the vehicle will not accelerate very rapidly, it will travel much further overall.
Go through the answers to the questions in Section 5 of the student workbook, especially question 8. Do the calculation of the mechanical advantage based on the actual length of the mousetrap arm and dowels or skewers teams were working with.
  Measure the length of your mousetrap spring arm in mm.
  Calculate the length of the arc through which the mousetrap arm travels as it closes. Remember that the circumference of a circle is 2𝜋𝑟 where 𝑟 is the radius of the circle.
  Note: some mousetraps do not operate over a full 180o. You may need to approximate the percentage of the semi-circle through which the arm does travel and multiply your answer by this amount. For example, if the arm travels through 90% of the semi-circle, multiply the answer by 0.9.
Circumference_(𝑠𝑒𝑚𝑖−𝑐𝑖𝑟𝑐𝑙𝑒)=〖𝐶𝑖𝑟𝑐𝑢𝑚𝑓𝑒𝑟𝑒𝑛𝑐𝑒〗_𝑐𝑖𝑟𝑐𝑙𝑒/2
Circumference_(𝑠𝑒𝑚𝑖−𝑐𝑖𝑟𝑐𝑙𝑒)=2𝜋𝑟/2=𝜋𝑟
3. If you connected the wheels of a vehicle directly to the mousetrap arm, what do you think would happen? How far would the vehicle travel?
The trap would snap shut very quickly, transferring its energy to the wheels very quickly. The wheels would accelerate rapidly but only for a very short period of time. It is likely that the wheels would just spin without driving the car forward very much, if at all.
4. Using the materials you have, create a device that will reduce the size of the output force and make it be applied over a greater distance.
Teams should figure out that if they extend the length of the mousetrap arm, they will increase the distance (and hence) time over which the force is applied and also decrease the force applied to the wheels.
5. If you have not yet done so, connect your dowel or skewer to the mousetrap arm with the cable ties or electrical tape. Which arm, the original arm or the extended arm travels through a greater distance?
The extended arm travels through a greater distance. Encourage students to trace, on a piece of paper, the arcs made by the end of the original arm and the extended arm to see that this is the case.
6. Is the force greater at the end of the original arm or the extended arm? Why?
The force is greater at the end of the original arm. The force at the end of the extended arm is being applied over a greater distance. For the work being done at both point to still be the same, the force must be reduced? Students should be able to feel this is the case by moving the trap from the end of the original arm and the end of the extended arm.
7. Measure the length of the extended arm and calculate the arc length through which the end travels.
Circumference_(𝑠𝑒𝑚𝑖−𝑐𝑖𝑟𝑐𝑙𝑒)=2𝜋𝑟/2=𝜋𝑟
8. We can think of the original arm as the input arm and the extended arm as the output arm. Calculate the mechanical advantage of this simple machine.
  𝑀𝐴=𝑟_(𝑜𝑟𝑖𝑔𝑖𝑛𝑎𝑙 𝑎𝑟𝑚)/𝑟_(𝑒𝑥𝑡𝑒𝑛𝑑𝑒𝑑 𝑎𝑟𝑚)
  9. By creating this simple lever machine with a mechanical advantage less than one, we increase the distance through which the output force is applied while decreasing the magnitude of this output force. How will this help us design a better mousetrap vehicle?
  It will reduce the force applied by the mousetrap to the wheels, preventing them from slipping and the vehicle wheel spinning. This reduced force is also applied over a greater distance meaning that we can drive the wheels for longer. While the vehicle will not accelerate very rapidly, it will travel much further overall.

## Slide 40
Notes: Ask the group which other part of their vehicle design could help them achieve additional mechanical advantage to further reduce the magnitude of the output force but increase the distance over it acts?
Explain that the same kind of mechanical advantage calculation can be done by comparing the radius of the axle to the radius of the wheels. The greater the difference, the greater the mechanical advantage (again, a reduction in force to gain a greater distance).
https://www.toppr.com/ask/question/which-of-the-following-is-an-example-of-a-wheel-and-axle-that-make-work/

## Slide 41: ಚಟುವಟಿಕೆ 4: ಸಂಭವನೀಯ ಪರಿಹಾರಗಳನ್ನು ರಚಿಸಿ
ಸಮಸ್ಯೆಯನ್ನು ಗುರುತಿಸಿ ಮತ್ತು ವಿವರಿಸಿ
ಸಮಸ್ಯೆಯನ್ನು ಗುರುತಿಸಿ ಮತ್ತು ವಿವರಿಸಿ
1
ಮಾಹಿತಿಯನ್ನು ಸಂಗ್ರಹಿಸಿ
2
ಸಂಭವನೀಯ ಪರಿಹಾರಗಳನ್ನು ರಚಿಸಿ
3
ಮೂಲಮಾದರಿಯನ್ನು ರಚಿಸಿ
4
ಮೂಲಮಾದರಿಯನ್ನು ಪರೀಕ್ಷಿಸಿ ಮತ್ತು ಮೌಲ್ಯಮಾಪನ ಮಾಡಿ
5
ಪರಿಹಾರ ಮಾರ್ಗವನ್ನು ಪರಿಷ್ಕರಿಸಿ ಮತ್ತು/ಅಥವಾ ಮರುವಿನ್ಯಾಸಗೊಳಿಸಿ
6
ಪರಿಹಾರ ಮಾರ್ಗವನ್ನು ಪ್ರಸ್ತುತಪಡಿಸಿ ಅಥವಾ ತಿಳಿಸಿ
7
ಸಂಭವನೀಯ ಪರಿಹಾರಗಳನ್ನು ರಚಿಸಿ
3

## Slide 42
Notes: Review the Engineering Design Process again and explain that the group is now ready to start generating possible solutions. They will start out generating as many different ideas as possible before evaluating these and deciding which one they will try first. Emphasize again that teams are welcome to return to any of the previous steps to understand the problem more clearly or gather additional information.
Watch the videos called d.school brainstorming rules (2:31) and how NOT to brainstorm (1:17).

## Slide 44
ಮುಕ್ತಚರ್ಚೆಯಲ್ಲಿ ಮಾಡಬೇಕಾದ ಮತ್ತು ಮಾಡಬಾರದ ನಿಯಮಗಳು
Notes: Now ask students to first spend a few moments completing Section 6 in their workbooks where they create their own list of brainstorming ‘do’s and don’ts’. Have students share their ideas with the whole group while you compile a master list. Make sure you get at least the following onto the list:
Value all ideas, even the crazy ones
Build off other ideas
Defer judgement
Aim for quantity over quality
Listen to each other

## Slide 45
ವಿಭಾಗ 7 ರ ಮೂಲಕ ಕೆಲಸ ಮಾಡಿ
Notes: As teams start the design process, have them work through the notes and resources available in Section 7 of their workbooks. This section will give them many helpful hints and tips.

## Slide 46
ವಿನ್ಯಾಸದ ಆಲೋಚನೆಗಳನ್ನು ರೂಪಿಸುವುದು
  ಸ್ಪ್ರಿಂಗ್‌ನಲ್ಲಿ ಸಂಗ್ರಹವಾಗಿರುವ ಶಕ್ತಿಯನ್ನು ವಾಹನದ ಚಕ್ರಗಳನ್ನು ತಿರುಗಿಸಲು ಹೇಗೆ ಬಳಸಬಹುದು?
  ಸ್ಪ್ರಿಂಗ್‌ನಲ್ಲಿರುವ ಶಕ್ತಿಯನ್ನು ನಿಧಾನವಾಗಿ ಮತ್ತು ನಿಯಂತ್ರಿತ ರೀತಿಯಲ್ಲಿ ಹೇಗೆ ಬಿಡುಗಡೆ ಮಾಡಬಹುದು?
  ವಾಹನವು ಅನುಭವಿಸುವ ಘರ್ಷಣೆಯನ್ನು ಹೇಗೆ ಕಡಿಮೆ ಮಾಡಬಹುದು?
  ವಾಹನವು ಮುಂದೆ ಚಲಿಸದೆ ಚಕ್ರಗಳು ಸುಮ್ಮನೆ ತಿರುಗುವುದನ್ನು ತಪ್ಪಿಸಲು, ಚಕ್ರ ಮತ್ತು ನೆಲದ ನಡುವೆ ಸಾಕಷ್ಟು ಎಳೆತವನ್ನು ಹೇಗೆ ಸೃಷ್ಟಿಸಬಹುದು?
  ವಾಹನವು ಸರಳ ರೇಖೆಯಲ್ಲಿ ಚಲಿಸುವುದನ್ನು ನಾವು ಹೇಗೆ ಖಚಿತಪಡಿಸಿಕೊಳ್ಳಬಹುದು?
  ಬಳಸಲು ಉತ್ತಮವಾದ ಸನ್ನೆಕೋಲಿನ ಉದ್ದ ಯಾವುದು?
  ವಾಹನದ ದ್ರವ್ಯರಾಶಿಯು (ತೂಕ) ಅದರ ಕಾರ್ಯಕ್ಷಮತೆಯ ಮೇಲೆ ಹೇಗೆ ಪರಿಣಾಮ ಬೀರುತ್ತದೆ?
  ಬಳಸಲು ಉತ್ತಮವಾದ ಚಕ್ರದ ಸರಿಯಾದ ಗಾತ್ರ ಯಾವುದು?
  ಚಕ್ರದ ದ್ರವ್ಯರಾಶಿಯು (ತೂಕ) ವಾಹನದ ಕಾರ್ಯಕ್ಷಮತೆಯ ಮೇಲೆ ಹೇಗೆ ಪರಿಣಾಮ ಬೀರುತ್ತದೆ?
  ನೀವು ಮುಂಭಾಗದ ಚಕ್ರದ ಚಾಲನೆ ಅಥವಾ ಹಿಂಭಾಗದ ಚಕ್ರದ ಚಾಲನೆ ವಿನ್ಯಾಸವನ್ನು ಬಳಸಲಿದ್ದೀರಾ?
  ನಿಮ್ಮ ಸನ್ನೆಕೋಲನ್ನು ಆಕ್ಸಲ್‌ಗೆ ಜೋಡಿಸಲು ಬಳಸಲು ಉತ್ತಮವಾದ ವಸ್ತು ಯಾವುದು?
  ಬಳಸಲು ಉತ್ತಮವಾದ ಆಕ್ಸಲ್‌ನ ವ್ಯಾಸ ಎಷ್ಟಿರಬೇಕು?
  ವಾಹನವು ಸರಳ ರೇಖೆಯಲ್ಲಿ ಚಲಿಸುವುದನ್ನು ನಾವು ಹೇಗೆ ಖಚಿತಪಡಿಸಿಕೊಳ್ಳಬಹುದು?
Notes: Have teams brainstorm and generate different possible design ideas for their mousetrap vehicles.
As students think about their designs, have them consider the following questions:
  How can the energy stored in the spring be used to turn the vehicle’s wheels?
  How can the energy stored in the spring be released in a slow and controlled manner?
  How can the friction experienced by the vehicle be reduced?
  How can enough traction between the wheels and the ground be created so that the wheels don’t just spin without the vehicle moving forward?
  How can we ensure the vehicle travels in a straight line?
  What is the best lever length to use?
  How will the mass of the vehicle affect its performance?
  What is the best size of wheel to use?
  How will the mass of the wheels affect the vehicle’s performance?
  Are you going to use a front or rear wheel drive design?
  What is the best material to use to attach your lever to your axle?
  What is the best diameter of axle to use?
  How can we ensure the vehicle travels in a straight line?

## Slide 47
ನಿಮ್ಮ ಆಲೋಚನೆಗಳನ್ನು ಚಿತ್ರಿಸಿ
Notes: Have teams to express their ideas in words and sketches and generate multiple different ideas (they can use Section 8 in their workbooks to capture these).
https://za.pinterest.com/pin/hand-drawn-idea-concept--529173024952906450/

## Slide 48: ರೇಸ್‌ನ ಸಮಯ!
ಸಹಿಷ್ಣುತೆಯ ಓಟ
ಒಂದು ಬಾರಿ 'ಚಾರ್ಜ್' ಮಾಡಿದಾಗ ಅತಿ ಹೆಚ್ಚು ದೂರ ಕ್ರಮಿಸುವ ಅಥವಾ ನಿರ್ದಿಷ್ಟ ಸಮಯದಲ್ಲಿ ಅತಿ ಹೆಚ್ಚು ಬಾರಿ ಚಾರ್ಜ್ ಮಾಡಿ ಹೆಚ್ಚು ದೂರ ಕ್ರಮಿಸುವ ವಾಹನ.
ವೇಗದ ಓಟ
ನಿರ್ದಿಷ್ಟ ದೂರವನ್ನು ಅತ್ಯಂತ ವೇಗವಾಗಿ ಕ್ರಮಿಸುವ ವಾಹನ.
Notes: Remind them that they are competing in two different races – an endurance race (the vehicle that travels the furthest) and a speed race (the vehicle that covers a set distance in the least time). Are they going to prioritize the needs of one race over the other or are they going to try and create a vehicle to take the overall title?

## Slide 49
Notes: Have teams use the Decision Matrix tool in Section 9 of their workbooks to compare and evaluate the different ideas to choose the best one(s). Remind teams that if this idea does not work out as expected, they can revisit their decision matrix to choose a different idea or come up with a totally new approach.

## Slide 50: ವಿನ್ಯಾಸದ ಸಂಕ್ಷಿಪ್ತ ವಿವರಣೆ
ವಿನ್ಯಾಸದ ಹೇಳಿಕೆ
ವಿವರಣಾತ್ಮಕ ರೇಖಾಚಿತ್ರಗಳು
ಸಾಮಗ್ರಿಗಳ ಪಟ್ಟಿ
Notes: To conclude this stage of the design process, have each team produce a design brief which describes their chosen design by completing Section 10 in their workbooks. The design brief includes:
  A design statement – a brief description of the chosen design solution.
  A set of detailed annotated sketches which describe the materials to be used, the important features of the design, how it will be constructed and an explanation of how it will work.
  A materials list.

## Slide 51: ಚಟುವಟಿಕೆ 5: ಮೂಲಮಾದರಿಯನ್ನು ರಚಿಸಿ
ಸಮಸ್ಯೆಯನ್ನು ಗುರುತಿಸಿ ಮತ್ತು ವಿವರಿಸಿ
ಸಮಸ್ಯೆಯನ್ನು ಗುರುತಿಸಿ ಮತ್ತು ವಿವರಿಸಿ
1
ಮಾಹಿತಿಯನ್ನು ಸಂಗ್ರಹಿಸಿ
2
ಸಂಭವನೀಯ ಪರಿಹಾರಗಳನ್ನು ರಚಿಸಿ
3
ಮೂಲಮಾದರಿಯನ್ನು ರಚಿಸಿ
4
ಮೂಲಮಾದರಿಯನ್ನು ಪರೀಕ್ಷಿಸಿ ಮತ್ತು ಮೌಲ್ಯಮಾಪನ ಮಾಡಿ
5
ಪರಿಹಾರ ಮಾರ್ಗವನ್ನು ಪರಿಷ್ಕರಿಸಿ ಮತ್ತು/ಅಥವಾ ಮರುವಿನ್ಯಾಸಗೊಳಿಸಿ
6
ಪರಿಹಾರ ಮಾರ್ಗವನ್ನು ಪ್ರಸ್ತುತಪಡಿಸಿ ಅಥವಾ ತಿಳಿಸಿ
7
ಮೂಲಮಾದರಿಯನ್ನು ರಚಿಸಿ
4

## Slide 52
Notes: Review the Engineering Design Process again and explain that the group is now ready to build its first prototype. Watch the video called What is a Prototype? (4:11) and then discuss the main features of a prototype. Explain that prototypes are used by engineers to test different ideas in the real world and to find out as quickly and cheaply which ideas work best. Explain that prototypes can be used to test one or more features of design.
Emphasize again that teams are welcome to return to any of the previous steps of the design process if they need to.

## Slide 53
Notes: Have students split into their teams to build their prototype vehicle. As teams work, remind them to refer to the Mouse Trap Cars: Construction Tips website for all sorts of design and construction tips.
https://techcommunity.microsoft.com/t5/azure-developer-community-blog/build-build-build-and-build-some-more-with-team-build/ba-p/335676

## Slide 54: ಚಟುವಟಿಕೆ 6: ಮೂಲಮಾದರಿಯನ್ನು ಪರೀಕ್ಷಿಸಿ ಮತ್ತು ಮೌಲ್ಯಮಾಪನ ಮಾಡಿ
ಸಮಸ್ಯೆಯನ್ನು ಗುರುತಿಸಿ ಮತ್ತು ವಿವರಿಸಿ
ಸಮಸ್ಯೆಯನ್ನು ಗುರುತಿಸಿ ಮತ್ತು ವಿವರಿಸಿ
1
ಮಾಹಿತಿಯನ್ನು ಸಂಗ್ರಹಿಸಿ
2
ಸಂಭವನೀಯ ಪರಿಹಾರಗಳನ್ನು ರಚಿಸಿ
3
ಮೂಲಮಾದರಿಯನ್ನು ರಚಿಸಿ
4
ಮೂಲಮಾದರಿಯನ್ನು (ಪ್ರೋಟೋಟೈಪ್‌) ಪರೀಕ್ಷಿಸಿ ಮತ್ತು ಮೌಲ್ಯಮಾಪನ ಮಾಡಿ
5
ಪರಿಹಾರ ಮಾರ್ಗವನ್ನು ಪರಿಷ್ಕರಿಸಿ ಮತ್ತು/ಅಥವಾ ಮರುವಿನ್ಯಾಸಗೊಳಿಸಿ
6
ಪರಿಹಾರ ಮಾರ್ಗವನ್ನು ಪ್ರಸ್ತುತಪಡಿಸಿ ಅಥವಾ ತಿಳಿಸಿ
7
ಮೂಲಮಾದರಿಯನ್ನು ಪರೀಕ್ಷಿಸಿ ಮತ್ತು ಮೌಲ್ಯಮಾಪನ ಮಾಡಿ
5

## Slide 55
Notes: Remind teams that failures are to be expected as this is what prototypes are for. Watch the video called Succeed by Failing (4:05) and discuss what the role of failure is in the design process. Discuss why it is important even if initial tests pass to keep testing and improving a design – a process called optimization. Refer to the examples of familiar products like smartphones, light bulbs or cars. Even though the first models may have worked just fine, these products have been continuously improved. Why?

## Slide 56: ನಿಮ್ಮ ವಿನ್ಯಾಸದ ಸವಾಲು
  ವಾಹನವು ಕನಿಷ್ಠ ಮೂರು ಚಕ್ರಗಳನ್ನು ಹೊಂದಿರಬೇಕು.
  ವಾಹನವನ್ನು ಒಂದು ಬಾರಿ 'ಚಾರ್ಜ್' ಮಾಡಿದಾಗ ಅದು ಕನಿಷ್ಠ 10 ಮೀಟರ್ (32.8 ಅಡಿ) ದೂರವನ್ನು ಕ್ರಮಿಸುವ ಸಾಮರ್ಥ್ಯ ಹೊಂದಿರಬೇಕು.
  ವಾಹನವನ್ನು ತಳ್ಳಿ ಚಾಲನೆ ಮಾಡುವುದಕ್ಕೆ ಅನುಮತಿ ಇರುವುದಿಲ್ಲ.
  ವಿದ್ಯಾರ್ಥಿಗಳು ನಿಗದಿತ ಸಮಯದಲ್ಲಿ ತಮ್ಮ ವಾಹನಗಳನ್ನು ವಿನ್ಯಾಸಗೊಳಿಸಬೇಕು ಮತ್ತು ನಿರ್ಮಿಸಬೇಕು.
ಮಾನದಂಡ
ಮಿತಿಗಳು
Notes: Discuss the kinds of tests that teams may want to perform by reviewing the success criteria for the challenge and reminding teams that their vehicles will compete in two different races:
  An endurance race to see which vehicle can cover the greatest distance on a single ‘charge’.
  A speed race to see which vehicle is fastest over a specific distance.

## Slide 57
ವಿವಿಧ ಚಕ್ರಗಳು, ಬಾಡಿ ವಿನ್ಯಾಸಗಳು ಅಥವಾ ಡ್ರೈವ್ ಟ್ರೈನ್‌ಗಳನ್ನು ಒಟ್ಟಿಗೆ ಪರೀಕ್ಷಿಸುವ ಬದಲು, ಪ್ರತಿ ಸಬ್-ಸಿಸ್ಟಮ್ ಅನ್ನು ಪ್ರತ್ಯೇಕವಾಗಿ ಪರೀಕ್ಷಿಸಲು ತಂಡಗಳಿಗೆ ಸೂಚಿಸಿ. ಇದರಿಂದ ಬದಲಾವಣೆಗಳ ಪರಿಣಾಮವನ್ನು ಗುರುತಿಸುವುದು ಸುಲಭವಾಗುತ್ತದೆ.
ಅತ್ಯುತ್ತಮ ವಿಧಾನವನ್ನು ನಿರ್ಧರಿಸುವ ಮೊದಲು, ಒಂದೇ ಸಮಸ್ಯೆಗೆ ಹಲವಾರು ವಿಭಿನ್ನ ವಿಧಾನಗಳನ್ನು ಪರೀಕ್ಷಿಸಿ ನೋಡಿ. ಅವರು ಎಳೆತವನ್ನು ಹೇಗೆ ಸುಧಾರಿಸಬೇಕೆಂದು ಪ್ರಯತ್ನಿಸುತ್ತಿದ್ದರೆ, ಯಾವುದಾದರೂ ಒಂದನ್ನು ಅಂತಿಮಗೊಳಿಸುವ ಮೊದಲು ವಿವಿಧ ಶ್ರೇಣಿಯ ಚಕ್ರ ವಿನ್ಯಾಸಗಳನ್ನು ಪರೀಕ್ಷಿಸಬೇಕು. ಕೆಲವು ಐಡಿಯಾಗಳು ಅವರಿಗೆ ಆಶ್ಚರ್ಯವನ್ನು ಉಂಟುಮಾಡಬಹುದು.
ಒಂದೇ ಸಮಸ್ಯೆಗೆ ವಿಭಿನ್ನ ಪರಿಹಾರಗಳನ್ನು ಪರೀಕ್ಷಿಸಿ
ಒಂದು ಬಾರಿಗೆ ಒಂದು ವಿಷಯವನ್ನು ಮಾತ್ರ ಪರೀಕ್ಷಿಸಿ
Notes: Explain that it is important that teams are structured in their testing approach. Therefore, encourage teams to test:
  One part at a time – rather than testing different wheels, body designs, or drive trains all at once, suggest that teams test each sub-system separately so that it is easier to discern the effects of different changes.
  Different solutions to the same problem – teams should test multiple different approaches to the same problem before deciding on the best approach. If they are looking at how to improve traction, they should test a range of different wheel designs before settling. Some ideas may surprise them.

## Slide 58
  ನಮ್ಮ ಪ್ರೋಟೋಟೈಪ್‌ನ ಯಾವ ಭಾಗವನ್ನು ನೀವು ಪರೀಕ್ಷಿಸುತ್ತೀರಿ?
  ನೀವು ಏನನ್ನು ಪರೀಕ್ಷಿಸುವಿರಿ? ನಿಮ್ಮ ತಂಡವು ಅನುಸರಿಸುವ ಪರೀಕ್ಷಾ ವಿಧಾನವು ಯಾವುದು?
  ನಮ್ಮ ಯಶಸ್ಸಿನ ಮಾನದಂಡವು ಯಾವುದು? ನಿಮ್ಮ ವಿನ್ಯಾಸವು ಕೆಲಸ ಮಾಡುತ್ತದೆಯೇ ಅಥವಾ ಇಲ್ಲವೇ ಎಂದು ನಿಮಗೆ ಹೇಗೆ ತಿಳಿಯುತ್ತದೆ? ಅಥವಾ ಅದರ ಯಾವ ಭಾಗಗಳನ್ನು ಸುಧಾರಿಸುವ ಅಥವಾ ಮರು-ವಿನ್ಯಾಸಗೊಳಿಸುವ ಅಗತ್ಯವಿದೆ ಎಂದು ತಿಳಿಯುವುದು ಹೇಗೆ?
  ನೀವು ಯಾವ ದತ್ತಾಂಶವನ್ನು ಸಂಗ್ರಹಿಸುತ್ತೇವೆ? ಈ ದತ್ತಾಂಶವನ್ನು ನೀವು ಹೇಗೆ ಸಂಗ್ರಹಿಸುತ್ತೇವೆ?
  ನಿಖರವಾದ ತೀರ್ಮಾನಕ್ಕೆ ಬರಲು ನೀವು ಈ ದತ್ತಾಂಶವನ್ನು ಹೇಗೆ ವಿಶ್ಲೇಷಿಸುತ್ತೇವೆ?
ಪರೀಕ್ಷೆಯ ಪ್ರಶ್ನೆಗಳು
Notes: Have students split into their teams but before they do any testing have them think about the following questions in Section 17 of their workbooks:
  What aspect(s) of their prototype will they test?
  How will they test? What testing procedure will they follow?
  What are their criteria for success? How will they know if their design works or not, or which parts of it need to be refined and/or redesigned?
  What data will they collect? How will they collect this data?
  How will they analyze this data to draw accurate conclusions?

## Slide 59
Notes: Have teams test their prototypes and collect and record their data. As they do, remind them that
  The engineering design process is iterative not linear. This means that it is about gradual testing, refinement, and improvement. Therefore, it is necessary to revisit earlier steps in the process.
  Failure is an essential part of the engineering design process. It is only through testing that we discover what works and how well it works. Never is a design perfect the first time.

## Slide 60
Notes: Using Section 12 of their workbooks, have teams start to describe the results of their tests.
  What worked and what failed?
  What were the problems encountered?
  What can be improved, changed or modified?
Remind teams that they can use the decision matrix if they need to decide between different new or modified design options.
Inform teams that, based on the improvements or changes they would like to make, they need to either start collecting the materials they will need or update their materials list if they need you to obtain any of these materials.
Also remind teams that they need to present their test data as part of their public presentations. Therefore, they need to record things like the total distance travelled or the total time travelled by different designs.

## Slide 61: ಚಟುವಟಿಕೆ 7: ಪರಿಹಾರ ಮಾರ್ಗವನ್ನು ಪರಿಷ್ಕರಿಸಿ ಮತ್ತು/ಅಥವಾ ಮರುವಿನ್ಯಾಸಗೊಳಿಸಿ
ಸಮಸ್ಯೆಯನ್ನು ಗುರುತಿಸಿ ಮತ್ತು ವಿವರಿಸಿ
ಸಮಸ್ಯೆಯನ್ನು ಗುರುತಿಸಿ ಮತ್ತು ವಿವರಿಸಿ
1
ಮಾಹಿತಿಯನ್ನು ಸಂಗ್ರಹಿಸಿ
2
ಸಂಭವನೀಯ ಪರಿಹಾರಗಳನ್ನು ರಚಿಸಿ
3
ಮೂಲಮಾದರಿಯನ್ನು ರಚಿಸಿ
4
ಮೂಲಮಾದರಿಯನ್ನು ಪರೀಕ್ಷಿಸಿ ಮತ್ತು ಮೌಲ್ಯಮಾಪನ ಮಾಡಿ
5
ಪರಿಹಾರ ಮಾರ್ಗವನ್ನು ಪರಿಷ್ಕರಿಸಿ ಮತ್ತು/ಅಥವಾ ಮರುವಿನ್ಯಾಸಗೊಳಿಸಿ
6
ಪರಿಹಾರ ಮಾರ್ಗವನ್ನು ಪ್ರಸ್ತುತಪಡಿಸಿ ಅಥವಾ ತಿಳಿಸಿ
7
ಪರಿಹಾರ ಮಾರ್ಗವನ್ನು ಪರಿಷ್ಕರಿಸಿ ಮತ್ತು/ಅಥವಾ ವಿವರಿಸಿ
6

## Slide 62
Notes: Have students split into their teams to make the necessary changes and refinements to their devices. For this design challenge you should expect teams to go through the design-test-redesign cycle about two to four times.
Have teams review Section 13 of their workbooks for some additional handy troubleshooting hints.
Be aware of the following dynamics in some teams or individuals and intervene as required.
  Aiming too high – some teams or individuals may wish to aim for perfection. Remind teams of the constraints of time and budget within which they are working and that, often, engineering is about finding the solution that best balances the criteria and constraints rather than the very best solution. This is sometimes termed ‘satisficing’ – the solution that meets the specifications and goals in an acceptably efficient and functional manner.
  Not aiming high enough – some teams or individuals may become demotivated or inclined to accept their very first design even if it does not adequately meet the criteria. Explain that the engineering design process is all about incremental improvement. Work with these teams to help them see how they can improve their designs and encourage them to keep pressing into the design process.
Image: https://www.shutterstock.com/search/redesigned

## Slide 63
Notes: As teams continue to test and refine their designs, have them start to work through the calculations in Section 14 of their workbooks. They will need to present these calculations in their final presentation.
https://stock.adobe.com/sk/search?k=calculate+button

## Slide 64: ಚಟುವಟಿಕೆ 8: ಪರಿಹಾರವನ್ನು ಪ್ರಸ್ತುತಪಡಿಸಿ
ಸಮಸ್ಯೆಯನ್ನು ಗುರುತಿಸಿ ಮತ್ತು ವಿವರಿಸಿ
ಸಮಸ್ಯೆಯನ್ನು ಗುರುತಿಸಿ ಮತ್ತು ವಿವರಿಸಿ
1
ಮಾಹಿತಿಯನ್ನು ಸಂಗ್ರಹಿಸಿ
2
ಸಂಭವನೀಯ ಪರಿಹಾರಗಳನ್ನು ರಚಿಸಿ
3
ಮೂಲಮಾದರಿಯನ್ನು ರಚಿಸಿ
4
ಮೂಲಮಾದರಿಯನ್ನು ಪರೀಕ್ಷಿಸಿ ಮತ್ತು ಮೌಲ್ಯಮಾಪನ ಮಾಡಿ
5
ಪರಿಹಾರ ಮಾರ್ಗವನ್ನು ಪರಿಷ್ಕರಿಸಿ ಮತ್ತು/ಅಥವಾ ಮರುವಿನ್ಯಾಸಗೊಳಿಸಿ
6
ಪರಿಹಾರ ಮಾರ್ಗವನ್ನು ಪ್ರಸ್ತುತಪಡಿಸಿ ಅಥವಾ ತಿಳಿಸಿ
7
ಪರಿಹಾರವನ್ನು ಪ್ರಸ್ತುತಪಡಿಸಿ
7

## Slide 65
Notes: Remind teams that they will present and demonstrate their mousetrap vehicles to a public audience. Watch the video called Good Presentation VS Bad Presentation (5:12) as a group for an illustration of some of the key differences between good and bad public presentations.

## Slide 66
Notes: You can also watch the video called TED's secret to great public speaking (7:56) for a more in-depth look into how ideas are spread to others when we speak. Pay particular attention to Chris’ four key tips.

## Slide 67
Notes: You can review the video How to avoid death By PowerPoint (20:31) and the article How to make a good presentation with 8 pro tips if you would like.
Video Link: https://youtu.be/Iwpi1Lm6dFo

## Slide 68
  ಘರ್ಷಣೆಗೆ ಸಂಬಂಧಿಸಿದಂತೆ ನೀವು ಎದುರಿಸಿದ ಸಮಸ್ಯೆಗಳು ಯಾವುವು ಮತ್ತು ನಿಮ್ಮ ತಂಡವು ಅವುಗಳನ್ನು ಹೇಗೆ ಪರಿಹರಿಸಿತು?
  ನೀವು ಯಾವ ರೀತಿಯ ಚಕ್ರಗಳನ್ನು ಬಳಸಿದಿರಿ? ನೀವು ಅವುಗಳನ್ನೇ ಏಕೆ ಆರಿಸಿಕೊಂಡಿದ್ದೀರಿ?
  ನಿಮ್ಮ ಮೌಸ್‌ಟ್ರ್ಯಾಪ್‌ನಲ್ಲಿ ಸಂಗ್ರಹವಾದ ಒಟ್ಟು ಅಂದಾಜು ಸ್ಥಿತಿಸ್ಥಾಪಕ (ಇಲಾಸ್ಟಿಕ್) ಅಂತಸ್ಥ ಶಕ್ತಿ (ಪೊಟೆನ್ಶಿಯಲ್ ಎನರ್ಜಿ) ಎಷ್ಟು?
  ವಾಹನದ ಒಟ್ಟು ಯಾಂತ್ರಿಕ ಪ್ರಯೋಜನ ಎಷ್ಟು?
  ವಾಹನವು ಚಾಲನೆಯಲ್ಲಿರುವಾಗ ಅದರ ವೇಗೋತ್ಕರ್ಷ ಎಷ್ಟಿತ್ತು?
  ನಿಮ್ಮ ಮೌಸ್‌ಟ್ರಾಪ್ ವಾಹನವು ತಲುಪಿದ ಗರಿಷ್ಠ ವೇಗ ಎಷ್ಟು?
  ನಿಮ್ಮ ವಾಹನವು ಕ್ರಮಿಸಬಹುದಾದ ಸೈದ್ಧಾಂತಿಕ ದೂರಕ್ಕೂ ಮತ್ತು ಅದು ವಾಸ್ತವವಾಗಿ ಕ್ರಮಿಸಿದ ದೂರಕ್ಕೂ ಇರುವ ಹೋಲಿಕೆ ಏನು ಮತ್ತು ಈ ವ್ಯತ್ಯಾಸಕ್ಕೆ ಕಾರಣವೇನು?
  ನಿಮ್ಮ ವಾಹನದ ಚಲನೆಗೆ ವಿರುದ್ಧ ದಿಕ್ಕಿನಲ್ಲಿ ಕಾರ್ಯನಿರ್ವಹಿಸುತ್ತಿದ್ದ ಘರ್ಷಣಾ ಬಲ ಎಷ್ಟಿತ್ತು?
  ಅಂತಸ್ಥ ಶಕ್ತಿಯನ್ನು ಚಲನಶಕ್ತಿಯನ್ನಾಗಿ ಪರಿವರ್ತಿಸುವಲ್ಲಿ ನಿಮ್ಮ ವಾಹನದ ಒಟ್ಟು ದಕ್ಷತೆ ಎಷ್ಟಿತ್ತು? ಹೆಚ್ಚಿನ ಆಪ್ಟಿಮೈಸೇಶನ್ ಮೂಲಕ ಇದನ್ನು ಹೇಗೆ ಸುಧಾರಿಸಬಹುದು?
ಸಾರ್ವಜನಿಕ ಪ್ರಸ್ತುತಿ
Notes: Remind teams that their presentation should include answers to the following questions:
  What problems related to friction did they encounter and how did they overcome these?
  What kind of wheels did they use? Why did they choose them?
  What was the total approximate elastic potential energy stored in their mousetrap?
  What was the total mechanical advantage of their vehicle?
  What was the work done by their vehicle in overcoming friction?
  What was the acceleration of their vehicle while under power?
  What was the maximum velocity achieved by their mousetrap vehicle?
  How did the theoretical distance their vehicle might have covered compare to the actual distance it covered and what was responsible for this difference?
  What was the force of friction acting in the opposite direction to the motion of their vehicle?
  What was the overall efficiency of their vehicle in converting potential energy to kinetic energy? How might this be improved through additional optimization?

## Slide 69
Notes: Have students divide into the teams and prepare their final presentations. They should have collected various pictures, video clips and notes that they can use to create their presentation and even include in it.
Remind teams that they should aim to present for no more than 10 minutes and that everyone in the team is expected to participate in the presentation.
Make sure that teams know when and where the presentations will take place.
Image: https://organizedbyellis.com/its-time-to-be-prepared/