## Slide 1: Spring Loaded
Engineering Academy | Unit 3

## Slide 2: Activity 1: Can a mousetrap be a battery?
Activity 1
Notes: https://commons.wikimedia.org/wiki/File:Victor-Mousetrap.jpg

## Slide 3
What is a battery?
Notes: Start by asking the group to describe and explain what a battery is.
https://www.engineersgarage.com/introduction-batteries-their-types/

## Slide 4
A device that converts stored chemical energy directly into electrical energy by means of a chemical reaction
Notes: One of the most common definitions is that a battery is a device that converts stored chemical energy directly into electric energy by means of a chemical reaction. Show the group the variety of batteries you have on hand.
https://www.officenational.com.au/shop/en/sba/duracell-alkaline-battery-coppertop-d

## Slide 5
What is the world’s biggest battery?
Notes: Now ask the group what they think the world’s biggest battery is. Where is it? What does it look like? How much power can it store?

## Slide 6
Notes: Play the video called The world's biggest battery looks nothing like a battery (5:15) which describes pumped hydro schemes as the world’s biggest batteries.

## Slide 7
How does a mousetrap work?
Notes: Now show the group a mousetrap and demonstrate how it works.
https://commons.wikimedia.org/wiki/File:Victor-Mousetrap.jpg

## Slide 8
Notes: Ask them whether they think this mousetrap can be thought of as a battery. Why or why not? You can facilitate this discussion using the following questions.
  What do batteries basically do? (They store energy.)
  What do you have to do to set the mousetrap? (You have use energy to push against the spring at set the trap.)
  What happens if you trigger the mousetrap? (The energy stored in the spring is released and the trap snaps shut.)
Explain that a mousetrap can be thought of as a battery. Batteries are basically just energy storage devices. We put energy into the battery, and it stays there until we release it. We must put energy in to bend the spring and set the mousetrap. This energy stays inside the spring until the mousetrap is triggered. Then all this energy is released very quickly as the trap snaps shut.

## Slide 9
Think about it
  If we can use a mousetrap as a battery, what else could we use as a battery? Where or how would the energy be stored?
  Could we design a car that runs on a mousetrap battery? What kinds of problems would we need to solve to make this possible?
  What else might we power with a mousetrap battery?
Notes: Split the group into their teams for this challenge and ask them to think about the following questions. They can note their answers in Section 1 of their workbooks.
If we can use a mousetrap as a battery, what else could we use as a battery? Where or how would the energy be stored?
Could we design a car that runs on a mousetrap battery? What kinds of problems would we need to solve to make this possible?
What else might we power with a mousetrap battery?
After about 10 min bring students back together and have them share and discuss their answers.

## Slide 10: Your design challenge
  The vehicle must have at least three wheels.
  The vehicle must be able to cover a minimum distance of 10 m (32.8 ft) on a single ‘charge’
  No push starts of vehicles are allowed.
  Students must design and build their vehicles within the given time.
Criteria
Constraints
Notes: Tell students that they are going to design and build a vehicle powered by a mousetrap. Describe the criteria and the constraints for the challenge and have teams write these down in Section 2 of their workbooks.
  Success criteria
    The vehicle must have at least three wheels.
    The vehicle must be able to cover a minimum distance of 10 m on a single ‘charge’.
  Constraints
    No push starts of vehicles are allowed.
    Students must design and build their vehicles within the given time.

## Slide 11: The Engineering Design Process
Identify and define the problem
1
Gather information
2
Generate possible solutions
3
Create prototype
4
Test and evaluate prototype
5
Refine and/or redesign solution
6
Present or communicate solution
7
Identify and define problem
1
Notes: Tell students that they will follow the engineering design process. If your students have never used the engineering design process before, hand out a copy of The Engineering Design Process to each team and take some time to explain the process and its steps.

## Slide 12: Race Time!
Endurance Race
The vehicle that covers the greatest distance on a single ‘charge’ or in a specific time with multiple charges.
Speed Race
The fastest vehicle over a specific distance.
Notes: Explain that teams will compete in races against other teams:
  An endurance race where prizes will be awarded for the vehicle that covers the greatest distance on a single ‘charge’.
  A speed race where prizes will be awarded for the fastest vehicle over a specific distance.

## Slide 13
Present your design solution and tell your design story
What problems related to friction did you encounter and how did your team overcome these?
What kind of wheels did you use? Why did you choose them?
What was the total approximate elastic potential energy stored in your mousetrap?
What was the total mechanical advantage of the vehicle?
What was the work done by your vehicle in overcoming friction?
What was the acceleration of the vehicle while under power?
What was the maximum velocity achieved by your mousetrap vehicle?
How did the theoretical distance the vehicle might have covered compare to the actual distance it covered and what was responsible for this difference?
What was the force of friction acting in the opposite direction to the motion of your vehicle?
What was the overall efficiency of the vehicle in converting potential energy to kinetic energy? How might this be improved through additional optimization?
Public presentation
Notes: Explain that teams will also present their vehicles to a public audience. This will also include them telling the story of their design, testing, and redesign process and presenting answers to the following questions:
  What problems related to friction did they encounter and how did they overcome these?
  What kind of wheels did they use? Why did they choose them?
  What was the total approximate elastic potential energy stored in their mousetrap?
  What was the total mechanical advantage of their vehicle?
  What was the work done by their vehicle in overcoming friction?
  What was the acceleration of their vehicle while under power?
  What was the maximum velocity achieved by their mousetrap vehicle?
  How did the theoretical distance their vehicle might have covered compare to the actual distance it covered and what was responsible for this difference?
  What was the force of friction acting in the opposite direction to the motion of their vehicle?
  What was the overall efficiency of their vehicle in converting potential energy to kinetic energy? How might this be improved through additional optimization?
Teams must also be prepared to answer questions on their design and the process they followed from members of the audience.
This presentation must be no more than 10 minutes.
Encourage teams to take pictures, record videos, and keep detailed notes of what they do and how they do it throughout the challenge. All this media and information will be especially useful come time to create their presentation.

## Slide 14: Activity 2: Identify and define the problem
Identify and define the problem
Identify and define the problem
1
Gather information
2
Generate possible solutions
3
Create prototype
4
Test and evaluate prototype
5
Refine and/or redesign solution
6
Present or communicate solution
7
Identify and define problem
1

## Slide 15
What is needed to make something move?
Notes: Start by facilitating a discussion with the group about what is needed to make an object move. Demonstrate this by having a student push a chair (or another object) across the floor. Say that to move the chair, the student must do work and to do work, the student needs to expend energy.
https://www.shutterstock.com/search/chair-race

## Slide 16
Energy is the ability to do work
Notes: Therefore, energy is defined as the “ability to do work”. The more work that must be done to move something, the more energy is needed.

## Slide 17
Kinetic energy
Notes: Explain that there are two main forms of energy – kinetic energy and potential energy.
  Kinetic energy is the energy of a moving object like a wrecking ball swinging into a house. It has kinetic energy enough to destroy a building. Demonstrate that a ball thrown through the air also has kinetic energy. If thrown at a window, it might have enough energy to break the window. Have the group give other everyday examples of things with kinetic energy.
  Potential energy is the energy that is stored because of the position or arrangement of matter. An example is a stationary wrecking ball held above a car. It is not doing any work on the car but sure has the potential to do some work if released. This is called gravitational potential energy (the potential energy of an object because of its position in Earth’s gravitational field). Demonstrate that a ball held above the ground also has gravitational potential energy that get converted into kinetic energy when released. Other types of potential energy include:

## Slide 18
Potential energy
Notes: Potential energy is the energy that is stored because of the position or arrangement of matter. An example is a stationary wrecking ball held above a car. It is not doing any work on the car but sure has the potential to do some work if released. This is called gravitational potential energy (the potential energy of an object because of its position in Earth’s gravitational field). Demonstrate that a ball held above the ground also has gravitational potential energy that get converted into kinetic energy when released.

## Slide 19: Main types of potential energy
The potential to do work by virtue of the object’s position above the ground
The energy stored in the chemical bonds between atoms and molecules.
the energy stored when an object, like a rubber band or spring is stretched or deformed.
the energy stored because of a charged particle’s position in an electric field or its position relative to another charged particle.
Gravitational Potential Energy
Chemical Potential Energy
Elastic Potential Energy
Electric Potential Energy
Notes: Chemical potential energy is the energy stored in the chemical bonds between atoms and molecules. Have the group give examples of everyday substances we use because of their chemical potential energy.
Elastic potential energy is the energy stored when an object, like a rubber band or spring is stretched or deformed. This energy is released when the object regains its normal shape. Have the group give other everyday examples of things able to store elastic potential energy.
Electric (or electromagnetic) potential energy is the energy stored because of a charged particle’s position in an electric field or its position relative to another charged particle. Demonstrate this by holding two opposite magnetic poles apart. As soon as we let go, this potential energy is converted into the kinetic energy of the magnets as they move together.

## Slide 20
Read Section 3 and do the calculations
Notes: Have teams read through Section 3 in their workbooks and do the simple calculations on kinetic energy.

## Slide 21: What is the kinetic energy of a 0.45 kg mousetrap vehicle moving at 3.2 m/s?
Notes: Spend a few minutes reviewing the answers to the questions from Section 3 in the student workbook with the group to make sure everyone understands how to work with the kinetic energy formula.

## Slide 22: A mousetrap vehicle has 1.46 J of kinetic energy. If it has a mass of 327 g, what is its velocity?

## Slide 23
Chemical potential
energy
Thermal energy
Kinetic energy
Notes: Explain that cars that use gasoline or petrol convert the chemical potential energy in the fuel into thermal energy in the cylinders which then gets converted into the kinetic energy of the pistons which ultimately turns the wheels and drives the car forward.
https://www.wonderopolis.org/wonder/what-is-gasoline-made-of
https://www.istockphoto.com/search/2/image?phrase=car+explosion
https://www.kbb.com/car-advice/horsepower-vs-torque/

## Slide 24
Read Section 4 and answer the questions
Notes: In this challenge we need to find a way to convert the elastic potential energy of a mousetrap into the kinetic energy of the vehicle.
Have teams read through Section 4 of their workbooks and then answer the questions.

## Slide 25
An object at rest will remain at rest unless an external force acts on it.
Friction (surface and fluid) works to stop all moving objects.
The greater the net force, the greater the acceleration or change in motion.
Unless a force greater than or equal to friction is applied an object will slow down.
Lighter objects accelerate faster for the same force.
The less friction, the smaller the force needed to accelerate an object.
The less friction, the less kinetic energy lost.
Key points
Notes: Go through the basic answers to the questions in Section 4 of the student workbook to make sure that everyone understands the basics of the laws of motion and friction. Here are some suggested answers for each question.
  An object, such as a car, at rest will remain at rest unless an external force acts on it.
  The reason moving cars don’t keep moving is because friction (surface and fluid) is constantly converting kinetic energy of the vehicle into heat and sound.
  If the engine of a car provides a force greater than friction (and air resistance), the car will accelerate and gain speed. The greater the net force, the greater the acceleration.
  Unless the engine continues to provide a force greater than friction (and air resistance), a car will slow down and eventually stop.
  Cars that are lighter will experience greater acceleration than heavier cars when the same net force is applied to them, or will need a smaller net force to achieve the same acceleration.
  The smaller the force of friction a car experiences, the smaller the force needed to accelerate the car (or change its motion).
  The smaller the force of friction a car experiences, the less kinetic energy will be lost to heat and sound and the farther the car will travel with a given force.

## Slide 26: Activity 3: Gather information
Identify and define the problem
Identify and define the problem
1
Gather information
2
Generate possible solutions
3
Create prototype
4
Test and evaluate prototype
5
Refine and/or redesign solution
6
Present or communicate solution
7
Gather information
2

## Slide 27
Mousetrap safety tips
  Never leave the trap set
  Never trigger the trap while holding it. Always lay it on a surface.
  Never trigger the trap with your finger. Always use a pen, pencil or other object.
Notes: Have students get into their teams and give each team its mousetrap for this challenge. Show students how to set and trigger the trap being very clear about the following safety rules:
  Never leave the trap set
  Never trigger the trap while holding it. Always lay it on a surface.
  Never trigger the trap with your finger. Always use a pen, pencil or other object.
Allow teams to practice setting and triggering the trap a few times making sure that everyone adheres to the three safety rules.
Ask teams to describe how the trap closes when triggered. Does it move quickly or slowly? Is the elastic potential energy in the spring released quickly of slowly? How far does the trap arm move when closing?
Have teams set and trigger their traps and ask them what would happen if they somehow connected the trap arms directly to the wheels of their vehicles. What do they think would happen? How far would their vehicles travel. How effective would this approach be?
Ask the group if anyone has any suggestions about how the elastic potential energy stored in the mousetrap can be released in a more controlled manner over a longer period.
https://www.canr.msu.edu/news/safety_awareness_to_prevent_later_injuries_to_others

## Slide 28
Notes: Play the video called The mighty mathematics of the lever (4:45) to the group that introduces and explains the concepts of levers.

## Slide 29
Notes: Emphasize that levers do not violate the laws of physics. We know that . If we extend the distance over which the force is applied to reduce the force, the total work is still the same. We have made a trade-off - reduced force but applied over a greater distance. Nothing is free!
Emphasize that levers do not violate the laws of physics. We know that 𝑊=𝐹×𝑑. If we extend the distance over which the force is applied to reduce the force, the total work is still the same. We have made a trade-off - reduced force but applied over a greater distance. Nothing is free!

## Slide 30
10 kg
5 kg
7 m
14 m
Notes: Work through the numerical example of this

## Slide 31
Notes: Explain that mechanical advantage is a measure of this trade-off and is the ratio of the output force to the input force. For a lever, it can also be expressed as the ratio of the distance of the input force from the fulcrum to the distance of the output force from the fulcrum.

## Slide 32
Mechanical advantage is the force or distance amplifying effect of a simple machine, like a
Lever
Inclined plane
Wheel and axle
Pulley system
Wedge
Screw
Notes: Simple machines - https://www.generationgenius.com/simple-machines-reading-material/ (fair use)

## Slide 33
OUTPUT:
Smaller force over greater distance
INPUT:
Larger force over smaller distance
Notes: Explain that the distance can also be measured as the distance over which the input and output forces travel.

## Slide 34
MA > 1
Output force > input force
Output distance < input distance
MA < 1
Output force < input force
Output distance > input distance
Notes: Explain that
  A mechanical advantage greater than one means that
    The output force is greater than the input force
    The output force travels a smaller distance than the input force
  A mechanical advantage less than one means that the output force
    The output force is less than the input force
    The output force travels a greater distance than the input force

## Slide 35
Notes: Explain that we can arrange a lever with both arms on the same side of the pivot. The force at the end of the shorter arm would be greater than the force at the end of the longer arm but it would travel through a smaller distance.
https://letstalkscience.ca/educational-resources/backgrounders/simple-machines-levers

## Slide 36
Notes: Explain that we can arrange a lever with both arms on the same side of the pivot. The force at the end of the shorter arm would be greater than the force at the end of the longer arm but it would travel through a smaller distance.

## Slide 38
Work through Section 5
Notes: Give each team a wooden dowel or skewer, some cable ties or electrical tape and a ruler and ask them to work through the steps in Section 5 of their workbooks to explore how they can change the mechanical advantage of their mousetraps.

## Slide 39
45 mm
295 mm
Notes: Go through the answers to the questions in Section 5 of the student workbook, especially question 8. Do the calculation of the mechanical advantage based on the actual length of the mousetrap arm and dowels or skewers teams were working with.
  Measure the length of your mousetrap spring arm in mm.
  Calculate the length of the arc through which the mousetrap arm travels as it closes. Remember that the circumference of a circle is where is the radius of the circle.
  Note: some mousetraps do not operate over a full 180o. You may need to approximate the percentage of the semi-circle through which the arm does travel and multiply your answer by this amount. For example, if the arm travels through 90% of the semi-circle, multiply the answer by 0.9.
3. If you connected the wheels of a vehicle directly to the mousetrap arm, what do you think would happen? How far would the vehicle travel?
The trap would snap shut very quickly, transferring its energy to the wheels very quickly. The wheels would accelerate rapidly but only for a very short period of time. It is likely that the wheels would just spin without driving the car forward very much, if at all.
4. Using the materials you have, create a device that will reduce the size of the output force and make it be applied over a greater distance.
Teams should figure out that if they extend the length of the mousetrap arm, they will increase the distance (and hence) time over which the force is applied and also decrease the force applied to the wheels.
5. If you have not yet done so, connect your dowel or skewer to the mousetrap arm with the cable ties or electrical tape. Which arm, the original arm or the extended arm travels through a greater distance?
The extended arm travels through a greater distance. Encourage students to trace, on a piece of paper, the arcs made by the end of the original arm and the extended arm to see that this is the case.
6. Is the force greater at the end of the original arm or the extended arm? Why?
The force is greater at the end of the original arm. The force at the end of the extended arm is being applied over a greater distance. For the work being done at both point to still be the same, the force must be reduced? Students should be able to feel this is the case by moving the trap from the end of the original arm and the end of the extended arm.
7. Measure the length of the extended arm and calculate the arc length through which the end travels.
8. We can think of the original arm as the input arm and the extended arm as the output arm. Calculate the mechanical advantage of this simple machine.
  9. By creating this simple lever machine with a mechanical advantage less than one, we increase the distance through which the output force is applied while decreasing the magnitude of this output force. How will this help us design a better mousetrap vehicle?
  It will reduce the force applied by the mousetrap to the wheels, preventing them from slipping and the vehicle wheel spinning. This reduced force is also applied over a greater distance meaning that we can drive the wheels for longer. While the vehicle will not accelerate very rapidly, it will travel much further overall.
Go through the answers to the questions in Section 5 of the student workbook, especially question 8. Do the calculation of the mechanical advantage based on the actual length of the mousetrap arm and dowels or skewers teams were working with.
  Measure the length of your mousetrap spring arm in mm.
  Calculate the length of the arc through which the mousetrap arm travels as it closes. Remember that the circumference of a circle is 2𝜋𝑟 where 𝑟 is the radius of the circle.
  Note: some mousetraps do not operate over a full 180o. You may need to approximate the percentage of the semi-circle through which the arm does travel and multiply your answer by this amount. For example, if the arm travels through 90% of the semi-circle, multiply the answer by 0.9.
Circumference_(𝑠𝑒𝑚𝑖−𝑐𝑖𝑟𝑐𝑙𝑒)=〖𝐶𝑖𝑟𝑐𝑢𝑚𝑓𝑒𝑟𝑒𝑛𝑐𝑒〗_𝑐𝑖𝑟𝑐𝑙𝑒/2
Circumference_(𝑠𝑒𝑚𝑖−𝑐𝑖𝑟𝑐𝑙𝑒)=2𝜋𝑟/2=𝜋𝑟
3. If you connected the wheels of a vehicle directly to the mousetrap arm, what do you think would happen? How far would the vehicle travel?
The trap would snap shut very quickly, transferring its energy to the wheels very quickly. The wheels would accelerate rapidly but only for a very short period of time. It is likely that the wheels would just spin without driving the car forward very much, if at all.
4. Using the materials you have, create a device that will reduce the size of the output force and make it be applied over a greater distance.
Teams should figure out that if they extend the length of the mousetrap arm, they will increase the distance (and hence) time over which the force is applied and also decrease the force applied to the wheels.
5. If you have not yet done so, connect your dowel or skewer to the mousetrap arm with the cable ties or electrical tape. Which arm, the original arm or the extended arm travels through a greater distance?
The extended arm travels through a greater distance. Encourage students to trace, on a piece of paper, the arcs made by the end of the original arm and the extended arm to see that this is the case.
6. Is the force greater at the end of the original arm or the extended arm? Why?
The force is greater at the end of the original arm. The force at the end of the extended arm is being applied over a greater distance. For the work being done at both point to still be the same, the force must be reduced? Students should be able to feel this is the case by moving the trap from the end of the original arm and the end of the extended arm.
7. Measure the length of the extended arm and calculate the arc length through which the end travels.
Circumference_(𝑠𝑒𝑚𝑖−𝑐𝑖𝑟𝑐𝑙𝑒)=2𝜋𝑟/2=𝜋𝑟
8. We can think of the original arm as the input arm and the extended arm as the output arm. Calculate the mechanical advantage of this simple machine.
  𝑀𝐴=𝑟_(𝑜𝑟𝑖𝑔𝑖𝑛𝑎𝑙 𝑎𝑟𝑚)/𝑟_(𝑒𝑥𝑡𝑒𝑛𝑑𝑒𝑑 𝑎𝑟𝑚)
  9. By creating this simple lever machine with a mechanical advantage less than one, we increase the distance through which the output force is applied while decreasing the magnitude of this output force. How will this help us design a better mousetrap vehicle?
  It will reduce the force applied by the mousetrap to the wheels, preventing them from slipping and the vehicle wheel spinning. This reduced force is also applied over a greater distance meaning that we can drive the wheels for longer. While the vehicle will not accelerate very rapidly, it will travel much further overall.

## Slide 40
Notes: Ask the group which other part of their vehicle design could help them achieve additional mechanical advantage to further reduce the magnitude of the output force but increase the distance over it acts?
Explain that the same kind of mechanical advantage calculation can be done by comparing the radius of the axle to the radius of the wheels. The greater the difference, the greater the mechanical advantage (again, a reduction in force to gain a greater distance).
https://www.toppr.com/ask/question/which-of-the-following-is-an-example-of-a-wheel-and-axle-that-make-work/

## Slide 41: Activity 4: Generate possible solutions
Identify and define the problem
Identify and define the problem
1
Gather information
2
Generate possible solutions
3
Create prototype
4
Test and evaluate prototype
5
Refine and/or redesign solution
6
Present or communicate solution
7
Generate possible solutions
3

## Slide 42
Notes: Review the Engineering Design Process again and explain that the group is now ready to start generating possible solutions. They will start out generating as many different ideas as possible before evaluating these and deciding which one they will try first. Emphasize again that teams are welcome to return to any of the previous steps to understand the problem more clearly or gather additional information.
Watch the videos called d.school brainstorming rules (2:31) and how NOT to brainstorm (1:17).

## Slide 44
The do’s and don’ts of brainstorming
Notes: Now ask students to first spend a few moments completing Section 6 in their workbooks where they create their own list of brainstorming ‘do’s and don’ts’. Have students share their ideas with the whole group while you compile a master list. Make sure you get at least the following onto the list:
Value all ideas, even the crazy ones
Build off other ideas
Defer judgement
Aim for quantity over quality
Listen to each other

## Slide 45
Work through Section 7
Notes: As teams start the design process, have them work through the notes and resources available in Section 7 of their workbooks. This section will give them many helpful hints and tips.

## Slide 46
Generate design ideas
  How can the energy stored in the spring be used to turn the vehicle’s wheels?
  How can the energy stored in the spring be released in a slow and controlled manner?
  How can the friction experienced by the vehicle be reduced?
  How can enough traction between the wheels and the ground be created so that the wheels don’t just spin without the vehicle moving forward?
  How can we ensure the vehicle travels in a straight line?
  What is the best lever length to use?
  How will the mass of the vehicle affect its performance?
  What is the best size of wheel to use?
  How will the mass of the wheels affect the vehicle’s performance?
  Are you going to use a front or rear wheel drive design?
  What is the best material to use to attach your lever to your axle?
  What is the best diameter of axle to use?
  How can we ensure the vehicle travels in a straight line?
Notes: Have teams brainstorm and generate different possible design ideas for their mousetrap vehicles.
As students think about their designs, have them consider the following questions:
  How can the energy stored in the spring be used to turn the vehicle’s wheels?
  How can the energy stored in the spring be released in a slow and controlled manner?
  How can the friction experienced by the vehicle be reduced?
  How can enough traction between the wheels and the ground be created so that the wheels don’t just spin without the vehicle moving forward?
  How can we ensure the vehicle travels in a straight line?
  What is the best lever length to use?
  How will the mass of the vehicle affect its performance?
  What is the best size of wheel to use?
  How will the mass of the wheels affect the vehicle’s performance?
  Are you going to use a front or rear wheel drive design?
  What is the best material to use to attach your lever to your axle?
  What is the best diameter of axle to use?
  How can we ensure the vehicle travels in a straight line?

## Slide 47
Draw your ideas
Notes: Have teams to express their ideas in words and sketches and generate multiple different ideas (they can use Section 8 in their workbooks to capture these).
https://za.pinterest.com/pin/hand-drawn-idea-concept--529173024952906450/

## Slide 48: Race Time!
Endurance Race
The vehicle that covers the greatest distance on a single ‘charge’ or in a specific time with multiple charges.
Speed Race
The fastest vehicle over a specific distance.
Notes: Remind them that they are competing in two different races – an endurance race (the vehicle that travels the furthest) and a speed race (the vehicle that covers a set distance in the least time). Are they going to prioritize the needs of one race over the other or are they going to try and create a vehicle to take the overall title?

## Slide 49
Notes: Have teams use the Decision Matrix tool in Section 9 of their workbooks to compare and evaluate the different ideas to choose the best one(s). Remind teams that if this idea does not work out as expected, they can revisit their decision matrix to choose a different idea or come up with a totally new approach.

## Slide 50: Design brief
Design statement
Annotated sketches
Materials list
Notes: To conclude this stage of the design process, have each team produce a design brief which describes their chosen design by completing Section 10 in their workbooks. The design brief includes:
  A design statement – a brief description of the chosen design solution.
  A set of detailed annotated sketches which describe the materials to be used, the important features of the design, how it will be constructed and an explanation of how it will work.
  A materials list.

## Slide 51: Activity 5: Create a prototype
Identify and define the problem
Identify and define the problem
1
Gather information
2
Generate possible solutions
3
Create prototype
4
Test and evaluate prototype
5
Refine and/or redesign solution
6
Present or communicate solution
7
Create prototype
4

## Slide 52
Notes: Review the Engineering Design Process again and explain that the group is now ready to build its first prototype. Watch the video called What is a Prototype? (4:11) and then discuss the main features of a prototype. Explain that prototypes are used by engineers to test different ideas in the real world and to find out as quickly and cheaply which ideas work best. Explain that prototypes can be used to test one or more features of design.
Emphasize again that teams are welcome to return to any of the previous steps of the design process if they need to.

## Slide 53
Notes: Have students split into their teams to build their prototype vehicle. As teams work, remind them to refer to the Mouse Trap Cars: Construction Tips website for all sorts of design and construction tips.
https://techcommunity.microsoft.com/t5/azure-developer-community-blog/build-build-build-and-build-some-more-with-team-build/ba-p/335676

## Slide 54: Activity 6: Test and evaluate prototype
Identify and define the problem
Identify and define the problem
1
Gather information
2
Generate possible solutions
3
Create prototype
4
Test and evaluate prototype
5
Refine and/or redesign solution
6
Present or communicate solution
7
Test and evaluate prototype
5

## Slide 55
Notes: Remind teams that failures are to be expected as this is what prototypes are for. Watch the video called Succeed by Failing (4:05) and discuss what the role of failure is in the design process. Discuss why it is important even if initial tests pass to keep testing and improving a design – a process called optimization. Refer to the examples of familiar products like smartphones, light bulbs or cars. Even though the first models may have worked just fine, these products have been continuously improved. Why?

## Slide 56: Your design challenge
  The vehicle must have at least three wheels.
  The vehicle must be able to cover a minimum distance of 10 m (32.8 ft) on a single ‘charge’
  No push starts of vehicles are allowed.
  Students must design and build their vehicles within the given time.
Criteria
Constraints
Notes: Discuss the kinds of tests that teams may want to perform by reviewing the success criteria for the challenge and reminding teams that their vehicles will compete in two different races:
  An endurance race to see which vehicle can cover the greatest distance on a single ‘charge’.
  A speed race to see which vehicle is fastest over a specific distance.

## Slide 57
Rather than testing different wheels, body designs, or drive trains all at once, suggest that teams test each sub-system separately so that it is easier to discern the effects of different changes.
Test multiple different approaches to the same problem before deciding on the best approach. If they are looking at how to improve traction, they should test a range of different wheel designs before settling. Some ideas may surprise them.
Test different solutions to the same problems
Test one thing at a time
Notes: Explain that it is important that teams are structured in their testing approach. Therefore, encourage teams to test:
  One part at a time – rather than testing different wheels, body designs, or drive trains all at once, suggest that teams test each sub-system separately so that it is easier to discern the effects of different changes.
  Different solutions to the same problem – teams should test multiple different approaches to the same problem before deciding on the best approach. If they are looking at how to improve traction, they should test a range of different wheel designs before settling. Some ideas may surprise them.

## Slide 58
  What aspect(s) of your prototype will you test?
  How will you test? What testing procedure will your team follow?
  What are the criteria for success? How will you know if your design works or not, or which parts of it need to be refined and/or redesigned?
  What data will you collect? How will you collect this data?
  How will you analyze this data to draw accurate conclusions?
Test questions
Notes: Have students split into their teams but before they do any testing have them think about the following questions in Section 17 of their workbooks:
  What aspect(s) of their prototype will they test?
  How will they test? What testing procedure will they follow?
  What are their criteria for success? How will they know if their design works or not, or which parts of it need to be refined and/or redesigned?
  What data will they collect? How will they collect this data?
  How will they analyze this data to draw accurate conclusions?

## Slide 59
Notes: Have teams test their prototypes and collect and record their data. As they do, remind them that
  The engineering design process is iterative not linear. This means that it is about gradual testing, refinement, and improvement. Therefore, it is necessary to revisit earlier steps in the process.
  Failure is an essential part of the engineering design process. It is only through testing that we discover what works and how well it works. Never is a design perfect the first time.

## Slide 60
Notes: Using Section 12 of their workbooks, have teams start to describe the results of their tests.
  What worked and what failed?
  What were the problems encountered?
  What can be improved, changed or modified?
Remind teams that they can use the decision matrix if they need to decide between different new or modified design options.
Inform teams that, based on the improvements or changes they would like to make, they need to either start collecting the materials they will need or update their materials list if they need you to obtain any of these materials.
Also remind teams that they need to present their test data as part of their public presentations. Therefore, they need to record things like the total distance travelled or the total time travelled by different designs.

## Slide 61: Activity 7: Refine and/or redesign solution
Identify and define the problem
Identify and define the problem
1
Gather information
2
Generate possible solutions
3
Create prototype
4
Test and evaluate prototype
5
Refine and/or redesign solution
6
Present or communicate solution
7
Define and/or redesign solution
6

## Slide 62
Notes: Have students split into their teams to make the necessary changes and refinements to their devices. For this design challenge you should expect teams to go through the design-test-redesign cycle about two to four times.
Have teams review Section 13 of their workbooks for some additional handy troubleshooting hints.
Be aware of the following dynamics in some teams or individuals and intervene as required.
  Aiming too high – some teams or individuals may wish to aim for perfection. Remind teams of the constraints of time and budget within which they are working and that, often, engineering is about finding the solution that best balances the criteria and constraints rather than the very best solution. This is sometimes termed ‘satisficing’ – the solution that meets the specifications and goals in an acceptably efficient and functional manner.
  Not aiming high enough – some teams or individuals may become demotivated or inclined to accept their very first design even if it does not adequately meet the criteria. Explain that the engineering design process is all about incremental improvement. Work with these teams to help them see how they can improve their designs and encourage them to keep pressing into the design process.
Image: https://www.shutterstock.com/search/redesigned

## Slide 63
Notes: As teams continue to test and refine their designs, have them start to work through the calculations in Section 14 of their workbooks. They will need to present these calculations in their final presentation.
https://stock.adobe.com/sk/search?k=calculate+button

## Slide 64: Activity 8: Present solution
Identify and define the problem
Identify and define the problem
1
Gather information
2
Generate possible solutions
3
Create prototype
4
Test and evaluate prototype
5
Refine and/or redesign solution
6
Present or communicate solution
7
Present solution
7

## Slide 65
Notes: Remind teams that they will present and demonstrate their mousetrap vehicles to a public audience. Watch the video called Good Presentation VS Bad Presentation (5:12) as a group for an illustration of some of the key differences between good and bad public presentations.

## Slide 66
Notes: You can also watch the video called TED's secret to great public speaking (7:56) for a more in-depth look into how ideas are spread to others when we speak. Pay particular attention to Chris’ four key tips.

## Slide 67
Notes: You can review the video How to avoid death By PowerPoint (20:31) and the article How to make a good presentation with 8 pro tips if you would like.
Video Link: https://youtu.be/Iwpi1Lm6dFo

## Slide 68
  What problems related to friction did you encounter and how did your team overcome these?
  What kind of wheels did you use? Why did you choose them?
  What was the total approximate elastic potential energy stored in your mousetrap?
  What was the total mechanical advantage of the vehicle?
  What was the acceleration of the vehicle while under power?
  What was the maximum velocity achieved by your mousetrap vehicle?
  How did the theoretical distance your vehicle might have covered compare to the actual distance it covered and what was responsible for this difference?
  What was the force of friction acting in the opposite direction to the motion of your vehicle?
  What was the overall efficiency of your vehicle in converting potential energy to kinetic energy? How might this be improved through additional optimization?
Public presentation
Notes: Remind teams that their presentation should include answers to the following questions:
  What problems related to friction did they encounter and how did they overcome these?
  What kind of wheels did they use? Why did they choose them?
  What was the total approximate elastic potential energy stored in their mousetrap?
  What was the total mechanical advantage of their vehicle?
  What was the work done by their vehicle in overcoming friction?
  What was the acceleration of their vehicle while under power?
  What was the maximum velocity achieved by their mousetrap vehicle?
  How did the theoretical distance their vehicle might have covered compare to the actual distance it covered and what was responsible for this difference?
  What was the force of friction acting in the opposite direction to the motion of their vehicle?
  What was the overall efficiency of their vehicle in converting potential energy to kinetic energy? How might this be improved through additional optimization?

## Slide 69
Notes: Have students divide into the teams and prepare their final presentations. They should have collected various pictures, video clips and notes that they can use to create their presentation and even include in it.
Remind teams that they should aim to present for no more than 10 minutes and that everyone in the team is expected to participate in the presentation.
Make sure that teams know when and where the presentations will take place.
Image: https://organizedbyellis.com/its-time-to-be-prepared/